## Slide 1: Electrical Principles
Topic 2: Electromagnetism

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Describe how a current through a conductor creates a magnetic field around the conductor
Describe how to increase the strength of the magnetic field produced around a current carrying conductor
Determine the direction of the magnetic field produced around a current carrying conductor
Describe the applications of the electromagnetic effect

## Slide 4: Unit 2.2: The Electromagnetic Effect

## Slide 5
Electricity and Magnetism - https://www.youtube.com/watch?v=N2yQYwlDkYI
Magnetism: Crash Course Physics - https://www.youtube.com/watch?v=s94suB5uLWw

## Slide 6: Introduction
We said in the last unit that electricity and magnetism are opposite sides of the same coin.
In this unit we will start to see why this is the case by exploring the electromagnetic effect – how a current flowing in a wire generates a magnetic field around the wire.
Notes: Img01 = photograph of a homemade electromagnet like https://www.sciencesource.com/Doc/TR1_WATERMARKED/5/5/0/f/SS2234028.jpg?d63641687627
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 7: Electromagnetic experiment
The best way for you to learn about the electromagnetic effect is for you to explore it for yourself. Here is a very simple experiment for you to try.
Click the button to download the instructions for doing the experiment. When you are done, you can watch the video of the experiment being done.
YT01
Instructions
Notes: Instructions = on click, open Doc01 in a new window. See appendix for brief.
YT01 = on click, play YT01 full screen. YT01 = https://www.youtube.com/watch?v=Zfv-0bQtqaE

## Slide 8: The main circuit
Once you have done the experiment a few times, take a video of you doing the experiment where you try to explain why you observe what you observe. Upload this video to your online profile.
Choose video
Upload
Notes: Img02 = https://cdn.pixabay.com/photo/2016/01/03/00/43/upload-1118929_960_720.png
Choose video = Launch file selection window
Upload = Upload file

## Slide 9: The electromagnetic effect
We saw in our experiment that when there was a current flowing through the wire, the magnetised needle was deflected. The only thing that would deflect a magnetised needle is another magnetic field.
This is the Electromagnetic Effect.
The Electromagnetic Effect:
A current flowing through a wire produces a magnetic field around the wire.

## Slide 10: The shape of the magnetic field
But what shape is this magnetic field? To find out, we can do another experiment as shown in this video.
Watch the video to learn about the shape of the magnetic field around a current carrying wire.
YT02
Notes: YT02 = on click, play YT02 full screen. YT02 = hthttps://v637g.app.goo.gl/Bta4qJQPazJaPAiv9

## Slide 11: The Right Hand Rule
The magnetic field formed around a current carrying wire is a set of concentric circles. We can work out which way the magnetic field lines go using the “right hand thumb rule”.
Point your right thumb in the direction of conventional current. Your fingers curl in the direction of the field lines.
Notes: Img03 = https://upload.wikimedia.org/wikipedia/commons/thumb/3/3e/Manoderecha.svg/2000px-Manoderecha.svg.png – marked for reuse

## Slide 12: The Right Hand Rule
Choose by clicking on the correct arrow, which way the field lines go if conventional current flows from left to right in the wire.
Notes: Multiple choice question
Correct answer is on the right.
Feedback
Correct – Excellent job
Incorrect – That is not right. Point your right thumb in the direction of the conventional current flow and your fingers will curl in the direction of the magnetic field.

## Slide 13: The arrow convention
To make it easier to visualise the direction of current flow and the resulting magnetic field, we use the arrow convention..
A dot represents conventional current flowing towards you OUT of the page like the tip of an arrow.
A cross represents conventional current flowing away from you INTO the page like the feathers of an arrow.
Notes: Img04 = redraw or source similar
Img05 = redraw or source similar

## Slide 14: Making a stronger magnetic field
One way to make the magnetic field around a wire stronger is to increase the current through it.
But another way is to turn the wire into a coil (called a solenoid). Then all the magnetic fields around each individual loop add up to a stronger overall field.
YT03
Watch the video to see the shape of the overall magnetic field.
Notes: YT03 = on click, play YT03 full screen. YT03 = hthttps://www.youtube.com/watch?v=BVIoEbC2l84

## Slide 15: Like a bar magnet
The resulting field lines of a solenoid look just like a bar magnet.
Notes: Ing06 = http://www.excelatphysics.com/uploads/3/1/7/5/31758667/1462103.jpg?558 – redraw but with very similar field lines

## Slide 16: Where’s North?
To work out where the North pole of the solenoid is, use the “right hand rule” again.
Curl your fingers in the direction of conventional current through the wire. Your thumb will point to the North pole.
Notes: Ing07 = Img11 from 07_01_01

## Slide 17: Solenoid Field Lines
This is what the field lines of a solenoid look like. Remember The dots represent current coming towards you and the crosses represent current going away from you.
Click on the side of the image where the north pole will be.
Notes: Img08 = Img12 from 07_01_01
Interaction: North is on the right side of the image. Provide following feedback:
Correct – well done. If you curl the fingers of your right hand in the direction of conventional current, your thumb will point to North (show image the correct hand position).
Incorrect – This is where the South pole will be. Remember, you need to use your right hand and you need to point your fingers in the direction of conventional current. The dots at the top tell us current is coming towards us. Have a look (show image of the correct hand position).

## Slide 18: Iron core
Notice how the field lines are most concentrated inside the solenoid. We can concentrate the field and make it even stronger by inserting an iron core into the solenoid.
Add an iron core
Notes: Img09 = part of Img06
Img10 = Img09 + iron rod inside solenoid + more field lines e.g. https://qph.fs.quoracdn.net/main-qimg-56e8620ea4eab70d4f0a7e0e29a3dd8e

## Slide 19: How To Make A Stronger Magnet
We can make the magnetic field resulting from the current flowing through a wire stronger in four ways.
Increase the current through the wire
Increase the number of turns in the coil
Wrap the wire around a soft iron core
1
3
3
Click on the numbers to see each point.
Turn the wire into a coil
2
Notes: Present boxes with just the number. On click/touch, reveal the full statement as a slide right animation
Display small animations to indicate that boxes can be clicked/touched

## Slide 20: What’s it good for?
So many things in modern life rely on the electromagnetic effect and the electromagnets it creates. One simple example is the electric bell.
Watch the video to learn how it works.
YT04
Notes: YT04 = on click, play YT04 full screen. YT04 = https://www.youtube.com/watch?v=nygn7wB7658

## Slide 21: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you understand what magnetism is.

## Slide 22: Question 1
Which diagram correctly depicts the magnetic field lines.
Img18
Img17
Img19
b)
c)
d)
Notes: Img11
Img12 = same as Img11 but with arrows on field lines in opposite direction
Img13 = same as Img11 but with no field lines going from N to S pole – all just go out into space
Img14 = Img11 but with some field lines crossing and joining
MCQ:
Correct answer: a
Feedback:
= Well done. That’s right. Field lines are always drawn from the north to the south pole and they never cross or join.
= That is not correct. Field lines are always drawn from the north to the south pole. The field lines in this diagram are going from south to north.
= That is not correct. Field lines always go from the north to south pole even if our diagram is not big enough to show the full line. In this diagram, even the field lines closest to the magnet do not form a closed path.
= That is not correct. Field lines never cross, touch or join.

## Slide 23: Question 2
Which diagram shows the weakest magnetic field.
Img16
b)
Notes: Img15
Img16 – same as Img15 but with double the field lines
MCQ:
Correct answer: a
Feedback:
= Well done. That’s right. The field lines in this diagram are further apart than in the other diagram. Another way to say this is that there are fewer field lines in area around the magnet than in the other diagram.
= That is not correct. The more field lines in a given area, the stronger the magnetic field. In this diagram there are more field lines in any given area around the magnet. Another way to say this is that the field lines are closer together.

## Slide 24: Question 3
Like poles…
Attract
Repel
Notes: MCQ:
Correct answer: b
Feedback:
= That is not correct. Like poles repel each other. Unlike poles attract.
= Well done. That’s right. Like poles repel.

## Slide 25: Question 4
True or false. Anything can be made into a permanent magnet.
True
False
Notes: MCQ:
Correct answer: b
Feedback:
= That is not correct. Only certain materials, called ferromagnetic materials, can be made into permanent magnets.
= Well done. Only certain materials, called ferromagnetic materials, can be made into permanent magnets.

## Slide 26: Question 5
Which expression gives the magnetic field strength?
Notes: MCQ:
Correct answer: c
Feedback:
= That is not correct. The expression for calculating the magnetic field strength is .
= That is not correct. While this expression is technically correct, it is not the expression for magnetic field strength. You would use this expression to calculate the magnetic flux.
= Well done. This is correct.
That is not correct. The expression for calculating the magnetic field strength is .
MCQ:
Correct answer: c
Feedback:
= That is not correct. The expression for calculating the magnetic field strength is 𝛽=𝜙/𝐴.
= That is not correct. While this expression is technically correct, it is not the expression for magnetic field strength. You would use this expression to calculate the magnetic flux.
= Well done. This is correct.
That is not correct. The expression for calculating the magnetic field strength is 𝛽=𝜙/𝐴.

## Slide 27: Document Briefing – Doc01 (1 of 3)
Create an annotated PDF worksheet with the following steps. Having pictures of each step of screen grabs from https://www.youtube.com/watch?v=Zfv-0bQtqaE would be beneficial.
Do do this experiment you will need
  2 polystyrene or paper cups
  A piece of thin wire
  A sewing needle
  Tape
  A 9V battery
  A bar magnet (the stronger the better but even a fridge magnet will do)
Start out by magnetising your sewing needle. Hold the bar magnet in your hand and rub the end of the magnet along the length of the needle a few times. The weaker your magnet, the more times you will need to rub it. Check that the needle is magnetised by trying to pick up a pin or some other small metal object.

## Slide 28: Document Briefing – Doc01 (2 of 3)
Next cut out the bottom of one of your cups so that you have a round flat disk and tape the magnetised needle to the disk through the centre. Taping the needle on top of a thick red line across the disk can make things easier later on.
Now fill the other cup with water and float the disk with the needle on it. It should orientate itself to North. If not, you will need to magnetise the needle more.
If your piece of wire has any plastic coating on in, you need to strip this off. You can use the blade of a knife or pair of scissors for this. Tape the one end of the wire to one of the terminals of your 9V battery.
Lay the wire over the cup parallel to the needle and connect the other end of the wire to the other battery terminal. Observe what happens to the needle. Why do you think this happens?

## Slide 29: Document Briefing – Doc01 (3 of 3)
Next, keep the wire laid over the cup parallel to the needle but this time reverse the battery connections i.e. connect each end to the other terminal and observe what happens to the needle. Why do you think this happened?
Lay the wire over the cup, but this time perpendicular (at right angles) to the needle and connect it to the battery. Observe what happens. Why do you think this happened?