## Slide 1: Electrical Principles
Topic 2: Electromagnetism

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Describe how a magnetic field around a conductor causes a current to flow through the conductor
Describe and explain Faraday’s Laws
Determine the direction of the magnetic field produced around a current carrying conductor
Describe the applications of the electromagnetic effect

## Slide 4: Unit 2.3: Electromagnetic Induction

## Slide 5
Electricity and Magnetism - https://www.youtube.com/watch?v=N2yQYwlDkYI
Magnetism: Crash Course Physics - https://www.youtube.com/watch?v=s94suB5uLWw

## Slide 6: Introduction
In the last unit we saw how passing a current through a conductor causes a magnetic field around the conductor.
But the reverse is also true.
A magnetic field around a conductor causes a current to flow through the conductor.
Img01
Notes: Img01 = Img01 from 07_01_01
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 7: Michael Faraday
Michael Faraday discovered electromagnetic induction in 1831 using a coil, galvanometer (used to measure small electric currents) and a permanent magnet.
Watch the video to learn more about his discovery.
YT01
Notes: YT01 = on click, play YT01 full screen. YT01 = https://www.youtube.com/watch?v=Hh58afwzHfA

## Slide 8: Experiment time
Time to do some experimenting of your own.
Click on the button to open the experiment instructions and then watch the video to see a summary of the experiment.
Vid01
Instructions
Notes: Instructions = on click, open Doc01. See appendix for brief
Vid01 = on click, play Vid01 full screen. See appendix for brief.

## Slide 9: Electromagnetic Induction
Let’s summarise the key points we know about electromagnetic induction so far.
Faraday’s First Law: When a conductor is placed in a changing magnetic field, an emf is induced in the conductor.
1
Click on the numbers to see each point.
Faraday’s Second Law: The magnitude of the emf is proportional to the rate at which the conductor cuts the magnetic field.
2t
Notes: Present boxes with just the number. On click/touch, reveal the full statement as a slide right animation
Display small animations to indicate that boxes can be clicked/touched

## Slide 10: Important points
Remember that electromagnetic induction will only happen if BOTH of these 2 specific conditions are met.
The conductor cuts through magnetic field lines.
The conductor experiences a changing magnetic field.
1
2
Click on each box for more details.
Notes: Box 1 = on click, open slide 11 in a pop-up
Box 2 = on click, open slide 12 in a pop-up

## Slide 11
The conductor must cut the magnetic field lines for an emf to be produced. The closer the angle at which it cuts them is to 90°, the greater will be the induced emf.
Img02
Notes: Img02 = see appendix for brief

## Slide 12
The conductor must experience a changing magnetic field. This can be achieved in three ways.
Img03
Img04
Img05
The conductor can move
The magnetic field can move
The magnetic field strength can change
Notes: Img03 = see appendix for brief
Img04 = see appendix for brief
Img05 = see appendix for brief

## Slide 13: How much emf is induced?
The amount of emf induced by electromagnetic induction, depends on three factors.
Strength of the magnetic field
The stronger the field, the greater the induced emf
1
Length of the conductor
The longer the conductor, the greater the induced emf
2
The speed at which the conductor cuts field lines
The greater the speed, the greater the induced emf
3

## Slide 14: Induced emf equation
If we consider the case where the magnetic field changes because either the field or the conductor is moving, we can combine all these factors into a nice simple equation.
Click on each symbol in the equation to find out more.
Notes: On click of each symbol in the equation, display the text below in a popup:
E = induced emf, measured in V (volts)
B = strength of the magnetic field (or magntic flux density) measured in T (teslas)
l = the length of the conductor, measured in m (meters)
v = the velocity of the conductor (or the field), measured in ms-1 (metres per second)

## Slide 15: Electromagnetic induction example
A wire 200mm long is moved through at a constant speed of 4m/s at right angles to its length through a uniform magnetic field. Calculate the density of the field if the emf generated in the wire is 0.15V.
Vid02
Try answering this question on your own first. Them watch the video for the full worked solution.
Notes: Vid02 = on click, play Vid02 full screen. See appendix for brief.

## Slide 16: A summary of electromagnetic induction
We have learnt quite a bit about electromagnetic induction so far. Let’s pause and review what we know.
Vid03
Watch the video for a full summary of everything we have learnt.
Notes: Vid03 = on click, play Vid03 full screen. See appendix for brief.

## Slide 17: The direction of the emf
One thing we have not touched on yet is the direction of the induced emf (or current). In the previous unit, we saw that if the current changed direction, the direction of the magnetic field also changed. Is the same true for electromagnetic induction?
Let’s do another experiment.
Click on the button to open the experiment instructions.
Instructions
Notes: Instructions = on click, open Doc02. See appendix for brief

## Slide 18: Fleming’s Right Hand Rule
We have just seen that if the polarity or direction of the magnetic field is changed, the direction of the induced emf (and current) is also changed.
To figure out the direction of the emf and ,therefore, the current, we use Flemings right-hand rule.
YT02
Watch the video to see how to use this rule to work out the direction of the current in the conductor.
Notes: YT02 = on click, play YT02 full screen. YT02 = https://www.youtube.com/watch?v=3vc2YEyHvJc

## Slide 19: Induced emf direction
Click on the image that indicates the correct direction of the induced emf or current in the conductor.
N
S
N
S
Notes: Multiple choice question
Img06 = on left
Img07 – on right
Correct answer is Img07
Feedback
Correct – That is not correct. If you hold the thumb, forefinger and middle finger of your right hand at 90° to each other and point your fore finger in the direction of the field and your thumb in the direction of the conductor’s motion, your middle finger will point towards you, indicating a current coming out of the screen.
Incorrect – Well done. If you hold the thumb, forefinger and middle finger of your right hand at 90° to each other and point your fore finger in the direction of the field and your thumb in the direction of the conductor’s motion, your middle finger will point towards you, indicating a current coming out of the screen.

## Slide 20: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you electromagnetic induction.

## Slide 21: Question 1
Which statement(s) about electromagnetic induction is/are NOT true?
The conductor must cut through magnetic field lines.
The conductor must experience a changing magnetic field.
The conductor must experience a magnetic field.
The emf induced in the conductor is inversely proportional to the rate at which the conductor cuts the magnetic field.
Notes: MCQ:
Correct answer: c and d
Feedback:
= This is not correct. This statement is TRUE. For there to be electromagnetic induction, the conductor must cut through magnetic field lines. There is no electromagnetic induction if the conductor is parallel to the magnetic field lines.
= This is not correct. This statement is TRUE. For there to be electromagnetic induction, there must be a changing magnetic field so that the conductor cuts magnetic field lines. This change can be achieved by either moving the conductor or magnetic field or by directly changing the strength of the magnetic field.
= Well done. This statement is FALSE. It is not enough for a conductor to experience a magnetic field. It must experience a changing magnetic field.
= Well done. This statements is FALSE. The induced emf is proportional to the rate at which the conductor cuts the field lines. The faster the conductor cuts the field lines, the greater the emf.

## Slide 22: Question 2
What will NOT result in a greater emf being inducted in a conductor.
Increase the strength of the magnetic field.
Increase the length of conductor cutting magnetic field lines.
Change the strength of the magnetic field more slowly.
Move the conductor through the magnetic field more quickly.
Notes: MCQ:
Correct answer: c
Feedback:
= This is not correct. The stronger the magnetic field, the greater the induced emf.
= This is not correct. The greater the length of conductor cutting through field lines, the greater the induced emf.
= Well done. Changing the strength of the magnetic field more slowly will mean that the conductor cuts the field lines more slowly and this will reduce the induced emf.
= This is not correct. Moving the conductor more quickly, will mean that it will cut the field lines more quickly and this will induce a greater emf.

## Slide 23: Question 3
In which case will the direction of the emf be out of the screen.
b)
Notes: MCQ:
Correct answer: a
Feedback:
= Well done. This is correct. If you point your index finger in the direction of the field and your thumb in the direction of the conductor’s motion, your middle finger will point in the direction of the induced emf.
This is not correct. If you point your index finger in the direction of the field and your thumb in the direction of the conductor’s motion, your middle finger will point in the direction of the induced emf.

## Slide 24: Question 4
In which case will the maximum emf be induced?
a)
b)
c)
Notes: MCQ:
Correct answer: a
Feedback:
= Well done. In this case the conductor cuts the field lines at close to 90°
= This is not correct. The angle at which the conductor cuts the field lines is less than that in a) so the induced emf will be less than in a).
= This is not correct. The angle at which the conductor cuts the field lines is less than that in a) so the induced emf will be less than in a).
MCQ:
Correct answer: c
Feedback:
= That is not correct. The expression for calculating the magnetic field strength is 𝛽=𝜙/𝐴.
= That is not correct. While this expression is technically correct, it is not the expression for magnetic field strength. You would use this expression to calculate the magnetic flux.
= Well done. This is correct.
That is not correct. The expression for calculating the magnetic field strength is 𝛽=𝜙/𝐴.

## Slide 25: Question 5
Arrange the North and South poles opposite each other to induce the maximum possible emf.
N
S
1
2
3
4
N
S
Notes: Drag and drop:
Correct answer indicated in blocks 3 and 4
Feedback:
If 1 = N and 2 = S OR if 1 = S and 2 = N: This is not correct. In this case, even though the conductor is moving, no emf will be induced because it will not cut any field lines.
If 4 = S and 3 = N: This is not correct. In this case, the conductor will cut the field lines at 90° so the induced emf will be a maximum but the induced will be into not out of the screen.
If 4 = N and 3 = S: Well done. In this case, the conductor will cut the field lines at 90° so the induced emf will be a maximum and will be in the correct direction i.e. out of the screen.

## Slide 26: Question 6
A coil moves at a constant speed of 5.5ms-1 through a uniform magnetic field of 0.105T and an emf of 230mV is induced. How long is the wire that makes up the coil?
365mm
398mm
398m
132mm
Notes: MCQ:
Correct answer: b
Feedback:
Correct = Well done.
Incorrect = That is not correct. E = Blv. Therefore, l = E/Bv = 0.23V/0.105T x 5.5ms-1 = 0.398m = 398mm

## Slide 27: Document Briefing – Doc01 (1 of 2)
Create an annotated PDF worksheet with the following steps.
Open up the interactive simulation of Faraday’s experiment at https://phet.colorado.edu/sims/html/faradays-law/latest/faradays-law_en.html.
Things will be easier to understand if you show the field lines. Turn these on by checking the Field lines checkbox.
Now click and drag the bar magnet slowly in and out of the coil of wire. What happens to the light bulb? What happens to the voltage in the circuit? What happens to the bulb and voltage when the magnet is stationary?
Move the bar magnet in and out of the coil more quickly. How does the brightness of the bulb compare to when you moved it slowly? How can you make the bulb shine most brightly?

## Slide 28: Document Briefing – Doc01 (2 of 2)
Now move the bar magnet slowly over the top of the coil. Does the lamp shine as brightly as before when you moved it at the same speed THROUGH the coil? Why do you think this is? What is different about how the field lines interact with the coil.
Click on the icon with 2 coils at the bottom of the screen.
Move the coil at the same speed in and out of each coil. When is the bulb the brightest. Why do you think this is?

## Slide 29: Video Briefing – Vid01 (1 of 2)
Create a screencast video using the interactive simulation at https://phet.colorado.edu/sims/html/faradays-law/latest/faradays-law_en.html to answer and explain the questions posed in Doc01.
Move the magnet slowly in and out of the coil to show that when the magnet is moving an EMF is produced which makes current flow in the circuit which makes the bulb shine.
Move the magnet more quickly so show that the faster the magnet moves the greater the EMF that is produced. Show that by moving the magnet very quickly, we can produce the greatest EMF.
But why does this happen? Explain that when the magnet moves, the field lines cut the coil which causes free electrons in the wire to be deflected at right angles to the field. Moving electrons = an electric current. The field lines cutting the wire exerts a force (which we call the electromotive force or force that moves electrons) on the electrons which moves them. Show https://www.youtube.com/watch?v=P3kJd3MDeuk to help with this explanation.

## Slide 30: Video Briefing – Vid01 (2 of 2)
Move the magnet through the coil again and show that the greatest emf is produced when the magnet enters and leave the coil because the field is strongest at the ends of the magnet. Strongest field = more field lines = more field lines cutting the coil = more force deflecting electrons = more emf.
Click the icon for both coils and show that greater emf produced with bigger coil. Same field strength but more coils. Therefore field lines cutting more coils = force exerted on more free electrons = greater emf.
Summarise by explaining that an emf is produced when field lines are cutting a wire. To make this happen, the field lines must move (i.e. the magnet must move) OR the wire mist move OR the strength of the magnetic field must be constantly changing. All these produce a changing magnetic field
When the wire is in a changing magnetic field, an emf is produced. The faster the change, the greater the emf. It is the field lines cutting the coil that induces an emf.

## Slide 31: Image Briefing – Img02 (1 of 3)
N
S
The orange conductor does not cut any of the field lines. Therefore, no emf will be produced.
Next >>
Produce the following set of three images with next, back navigation.
No emf

## Slide 32: Image Briefing – Img02 (2 of 3)
N
S
The orange conductor cuts some of the field lines. Therefore, an emf will be produced.
Next >>
<< Back
Some emf

## Slide 33: Image Briefing – Img02 (3 of 3)
N
S
The orange conductor cuts the field lines at right angles. Therefore, a a maximum emf will be produced.
<< Back
Max emf

## Slide 34: Image Briefing – Img03
N
S
Produce an animated gif where the orange conductor moves right and left.

## Slide 35: Image Briefing – Img04
N
S
Produce an animated gif where the magnetic field moves left and right.

## Slide 36: Image Briefing – Img05
N
S
Produce an animated gif where the magnetic field gets stronger and weaker (both extremes represented).
N
S

## Slide 37: Video Briefing – Vid02 (1 of 2)
Create a screencast video answering the question.
Note the conversion of 200mm to metres.

## Slide 38: Video Briefing – Vid03 (1 of 2)
Create a screencast video using the interactive simulation at https://phet.colorado.edu/en/simulation/legacy/faraday.
Open the pickup coil tab.
Set the strength to 50%, loop area to 50%, loops = 1, show field – move magnet in and out of the loop quickly and slowly to show difference in emf produced – greater the speed of magnet = greater rate of change of magnetic field = greater emf.
Change loops to 3 – move magnet in and out to show that more loops (or longer the wire) more electrons are deflected = greater emf.
Change magnet strength to 25% and then 100% to show that the greater the strength of the field, the greater the emf.
Say that so far, we have moved the magnet but we can also induce an emf if we move the wire – demonstrate this. In either case, wire will cut field lines and will experience a changing magnetic field.

## Slide 39: Video Briefing – Vid03 (1 of 2)
We can also create a changing magnetic field directly changing the strength of the magnetic field – demonstrate this

## Slide 40: Document Briefing – Doc02 (1 of 2)
Create an annotated PDF worksheet with the following steps.
Open up the interactive simulation of Faraday’s experiment at https://phet.colorado.edu/sims/html/faradays-law/latest/faradays-law_en.html.
Things will be easier to understand if you show the field lines. Turn these on by checking the Field lines checkbox.
Now click and drag the bar magnet slowly in and out of the coil of wire. Notice the direction of the voltage as the magnet moves into the coil.
Now swop the magnet around and do the same thing. What do you notice about the direction of the voltage now as the magnet moves into the coil?