## Slide 1: Electrical Principles
Topic 3: Solving DC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Calculate current, voltage, resistance and power in circuit in combination circuits.

## Slide 4: Unit 3.3: Combination Circuits

## Slide 5: Introduction
So far in this topic, we have looked at series circuits and parallel circuits.
In this unit, we are going to solve combination circuits – circuits that have series and parallel elements.
Click on different parts of the image to learn more.
Notes: Img01 = https://www.electronicshub.org/wp-content/uploads/2014/12/5.-Resistors-in-Combination-Circuit.png
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Series and parallel circuits
Before we begin, let’s quickly revise what we know about series and parallel circuits.
Parallel Circuit
Series Circuit
Click on each circuit for a summary of what we know.
Notes: Img02 = Img02 from 01_03_02 without the arrows, nodes and labels
Img03 = Img03 from 01_03_02 without arrows
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 7: Series circuit summary
In a series circuit the following are true.
RT = R1 + R2 + R3
IT = I1 = I2 = I3
VT = V1 + V2 + V3
Img04
Img06 from 01_03_01
Notes: Img04 = Img06 from 01_03_01
Duplicate slide 17 from 01_03_01
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 8: Parallel circuit summary
In a parallel circuit the following are true.
IT = I1 + I2 + I3
VT = V1 = V2 = V3
Img05
Img05 from 01_03_02
Notes: Img05 = Img05 form 01_03_02
Duplicate slide 12 from 01_03_02
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Remember power
Also, remember that we can calculate the power dissipated in a circuit using any of the following three expressions
P = V x I
But V = I x R
∴ P = (I x R) x R
∴ P = I2 x R
But I = V/R
∴ P = V x (V/R)
∴ P = V2/R
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: Solving combination circuits – example 1
Let’s start with this example.
Redraw the circuit on a blank piece of paper.
In this circuit, calculate the:
Total resistance
Voltage drop across R1, R3 and R4
Current through R2, R3 and R5
10Ω
15Ω
18Ω
6Ω
12Ω
22Ω
VT = 12V
Notes: Img06 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 11: Solving series circuits – step 1
Click on the image to see a full screen version of how you should label your circuit.
Once you have drawn the basic circuit, you need to label it. When dealing with combination circuits, it is important that you label it correctly. This will help later on.
Img07
Notes: Img07 = on click, display Img07 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 12: Did you notice?
Click on the button to see the answers.
Just by looking at your labeled image, what can you say about
I3
V1 and V2
V4, V5 and V6?
Img07
Answers
Notes: Img07
Answers = on click, present the following in a popup.
I3 = IT (Kirchoff’s current law
V1 = V2 = V1 (voltage is the same over resistors in parallel)
V4 = V5 = V6 = V2 (voltage is the same over resistors in parallel)
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 13: Solving combination circuits – step 2
When dealing with combination circuits, the basic strategy is to make them into series circuits by finding the equivalent series resistances of all the parallel parts.
Check
Calculate the resistances of R∥1
and R∥2.
R∥1
Ω
R∥2
Ω
=10Ω
=15Ω
=18Ω
=6Ω
=12Ω
=22Ω
VT = 12V
IT
I1
I2
I3
I4
I5
I6
V∥1
V∥2
R∥1
R∥2
V1
V2
V4
V5
V1
Notes: Img07
Fill in the blank question
Correct answers: R∥1=6Ω | R∥2=3.385Ω
Feedback:
Correct – Well done. You got those calculations right.
Incorrect – That is not correct. Here are the correct calculations. R∥1=. R∥2=
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 14: Solving combination circuits – step 3
Now that we have calculated the equivalent resistances of the parallel parts, we can redraw the circuit as a series circuit.
Redraw your circuit as a series circuit and then click on the image to see a full screen version of what your circuit should look like.
Img08
Notes: Img08 = on click, display Img08 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 15: Solving combination circuits – step 4
R∥1=6Ω
R3=18Ω
R∥2=3.385Ω
VT = 12V
IT
I3
V∥1
V∥2
V3
Finally, we can answer the questions. The first question asked you to calculate the total resistance.
Calculate the total resistance in the circuit.
Check
Ω
Notes: Img08
Fill in the blank question
Correct answer: 27.385Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 16: Solving combination circuits – step 4
R∥1=6Ω
R3=18Ω
R∥2=3.385Ω
VT = 12V
IT
I3
V∥1
V∥2
V3
Calculate the voltage drop across R1, R3 and R4.
Check
V1
V
V3
V
V4
V
Check
Check
See the full worked solution
Notes: Img08
Fill in the blank question
Correct answers: V1 = 2.628V | V3 = 7.884V | V4 = 1.483V
Feedback:
V1
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
V3
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
V4
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
See the full worked solution = only display ater all answers have been submitted. On click, play Vid01 full screen. See appendix for Vid01.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 17: Solving combination circuits – step 4
R∥1=6Ω
R3=18Ω
R∥2=3.385Ω
VT = 12V
IT
I3
V∥1
V∥2
V3
Calculate the current through drop across R2, R3 and R5.
Check
I2
A
I3
A
I5
A
Check
Check
See the full worked solution
Notes: Img08
Fill in the blank question
Correct answers: I2 = 0.175A | I3 = 0.438A | I5 = 0.124A
Feedback:
V1
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
V3
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
V4
Correct – Well done. You got it!
Incorrect – That is not correct. Watch the video to see the full worked solution.
See the full worked solution = only display ater all answers have been submitted. On click, play Vid02 full screen. See appendix for Vid02.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 18: Solving combination circuits – example 2
VT
IT=9A
R1=18Ω
R2=42Ω
R3=34Ω
Full worked solution
In this circuit, calculate the:
Resistance of the parallel section
Total resistance;
Power consumed by R1;
Total voltage; and
Voltage across the parallel section.
Try the question on your own and then watch the full worked solution.
Notes: Img09 – redraw
Full worked solution = on click, play Vid03 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 19: Solving combination circuits – example 3
Full worked solution
In this circuit, calculate the:
Total resistance in the circuit;
Total current flowing in the circuit; and
The voltage drop across the 950Ω resistor.
Try the question on your own and then watch the full worked solution.
790Ω
800Ω
630Ω
900Ω
200V
950Ω
Hint
Notes: Img10 – redraw
Full worked solution = on click, play Vid04 full screen. See appendix for brief
Hint = on click, display slide 20 in a popup
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 20
This circuit may seem very unusual but it is just an ordinary combination circuit. The first thing you should do is redraw it in the more recognizable combination circuit form.
790Ω
800Ω
630Ω
900Ω
200V
950Ω
800Ω
630Ω
790Ω
950Ω
900Ω
200V
Notes: Img11 = redraw
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 21: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you understand resistors in combination circuits.
Notes: See 01_03_03_Activity for the original questions. Doc01 = This document must also be formatted into a downloadable worksheet. The memo is 01_03_03_Activity Solutions – see appendix for brief

## Slide 22: Question 1
Two resistors R1 and R2 with values of 15Ω and 10Ω respectively are connected in parallel. This combination is then connected in series to a third resistor, R3, which has a value of 5Ω. The complete circuit is supplied by a 100V DC power source.

## Slide 23: Question 1
1.1:
Calculate the resistance of the parallel combination and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct answer: 6Ω
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 24: Question 1
1.2:
Calculate the total resistance of the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 11Ω
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 25: Question 1
1.3:
Calculate the total current in the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 9.091A
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 26: Question 1
1.4:
Calculate the power dissipated by the parallel combination and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 495.878W
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 27: Question 1
1.5:
Calculate voltage drop across R3 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 45.455V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 28: Question 2
Study the circuit and then answer the questions that follow.

## Slide 29: Question 2
2.1:
Calculate the total resistance (RT) of the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 875Ω
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 30: Question 2
2.2:
Calculate the current IR2 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 0.013A or 13mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 31: Question 2
2.3:
Calculate the voltage drop VR2 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 6.5V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 32: Question 2
2.4:
Calculate the voltage drop VR1 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 4.5V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 33: Question 2
2.5:
Calculate the value of the current IR1 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 0.005A or 4.5mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 34: Question 2
2.6:
Calculate the power consumed by the resistor R4 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 32.5mW or 0.033W
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 35: Question 3
The DC circuit has a supply voltage of 60V. A voltmeter is connected across the 2K2Ω resistor. Analyse the circuit and then answer the following questions.

## Slide 36: Question 3
3.1:
Calculate the total resistance of the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 468.613Ω
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 37: Question 3
3.2:
Calculate the total current in the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 0.128A or 128mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 38: Question 3
3.3:
Calculate the voltage across the 2K2Ω resistor and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 36.96V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 39: Question 4
Study the circuit and then answer the question that follow.

## Slide 40: Question 4
4.1:
Calculate the total resistance (RT) of the circuit and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 570.61Ω
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 41: Question 4
4.2:
Calculate the value of the current IR4 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 0.032A or 32mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 42: Question 4
4.3:
Calculate the value of the voltage drop VR4 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 3.2V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 43: Question 4
4.4:
Calculate the value of the voltage drop VR5 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 8.64V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 44: Question 4
4.5:
Calculate the value of the voltage drop VR3 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 6.42V
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 45: Question 4
4.6:
Calculate the value of the current IR1 and enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct Answer: 0.018A or 18mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_03_Activity Solutions for full worked solution.

## Slide 46: Image Briefing – Img07
When working with combination circuits, you must also label the portions of the circuit that are in parallel. In this case, we have labeled them R∥1 and R∥2.
=10Ω
=15Ω
=18Ω
=6Ω
=12Ω
=22Ω
VT = 12V
IT
I1
I2
I3
I4
I5
I6
V∥1
V∥2
R∥1
R∥2
V1
V2
V4
V5
V1

## Slide 47: Image Briefing – Img08
R∥1=6Ω
R3=18Ω
R∥2=3.385Ω
VT = 12V
IT
I3
V∥1
V∥2
V3

## Slide 48: Video Briefing – Vid01
Create a screencast video presented by an expert presenter. The presenter needs to work through the calculations for calculating the voltage drop across R1, R3 and R4.

## Slide 49: Video Briefing – Vid02
Create a screencast video presented by an expert presenter. The presenter needs to work through the calculations for calculating the voltage drop across I1, I3 and I5.

## Slide 50: Video Briefing – Vid03
Create a screencast video presented by an expert presenter. The presenter needs to work through example 2 as follows, using the Img08 as a basis. Check the answers with http://http://everycircuit.com/circuit/5047957555773440.
V1

## Slide 51: Video Briefing – Vid04 (1 of 2)
Create a screencast video presented by an expert presenter. The presenter needs to work through example 2 as follows, using the Img08 as a basis. Check the answers with http://everycircuit.com/circuit/4915314839257088.
First redraw the circuit…

## Slide 52: Video Briefing – Vid04 (2 of 2)

## Slide 53: Document Briefing – Doc01
Create a worksheet based on 01_03_03_Activity and a worked solutions memo based on 01_03_03_Activity Solutions