## Slide 1: Electrical Principles
Topic 3: Solving DC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Explain and apply Kirchoff’s current law and Kirchoff’s voltage law in combination circuits.

## Slide 4: Unit 3.4: Kirchoff’s Laws in ombination Circuits

## Slide 5: Introduction
In the last unit, we got some practice solving simple combination circuits.
In this unit, we are going to learn how to apply Kirchoff’s Voltage and Current Laws to solve more complicated combination circuits.
Click on each button to see a reminder of each of these laws.
Kirchoff’s Current Law
Kirchoff’s Voltage Law
Notes: Kirchoff’s Current Law = on click, present slide 6 as a popup
Kirchoff’s Voltage Law = on click, present slide 7 as a popup
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Kirchoff’s current law
The sum of the currents entering a node or junction is equal to the sum of the currents leaving the node or junction.
This is also called the First Law and applies to parallel circuits.
IT
IT
I1
I2
I3
R1
R2
R3
IT = I1 + I2 + I3
Notes: Img01 - redraw
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 7: Kirchoff’s voltage law
R1
R2
R3
V3
V2
V1
VT
The sum of the voltage drops in a closed circuit is equal to the applied circuit voltage.
This is also called the Second Law and applies to series circuits.
VT = V1 + V2 + V3
Notes: Img02 = based on Img12 from 01_03
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 8: Solving circuits using Kirchoff – example 1
Try this question on your own. Start by redrawing the circuit on a blank piece of paper. When you are done, watch the full worked solution.
In this circuit, calculate the current through R1 and R2.
VT=24V
R1=6Ω
R2=8Ω
R3=12Ω
R4=4Ω
See the full worked solution
Notes: Img03 – redraw
See the full worked solution = on click, play Vid01 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Solving circuits using Kirchoff – example 2
Use Kirchoff’s laws to determine the values of I1 and I2. Only use loops DABCD and DACD.
VT=12V
4Ω
I1
I2
8Ω
6Ω
8Ω
2Ω
4Ω
0.9A
I1 - 0.9A
I1 – I2
Try this example on your own first and then watch the full worked solution.
See the full worked solution
D
A
B
C
Notes: Img04 = Redraw
See the full worked solution = on click, play Vid02 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: Solving circuits using Kirchoff – example 3
Determine, with the aid of Kirchoff’s laws:
The equation for loop ABDA;
The equation for loop BCDB; and
I1 and I2
Try this example on your own first and then watch the full worked solution.
See the full worked solution
A
B
C
D
VT=12V
R1=10Ω
R2=15Ω
R3=20Ω
R4=25Ω
R5=5Ω
IT
I1
I2
0.012A
I2+0.012A
I1-0.012A
Notes: Img05 = Redraw
See the full worked solution = on click, play Vid03 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 11: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you understand Kirchoff’s Laws in combination circuits.
Notes: See 01_03_04_Activity for the original questions. Doc01 = This document must also be formatted into a downloadable worksheet. The memo is 01_03_04_Activity Solutions – see appendix for brief

## Slide 12: Question 1
Kirchoff’s first law is applicable to
Series circuits
Parallel circuits
Series-parallel circuits
Notes: MCQ
Correct answer: b
Feedback:
Correct – Well done. That is correct.
Incorrect – That is not correct. Kirchoff’s first law is the current law. The voltage law is called Kirchoff’s second law.

## Slide 13: Question 2
Which definition of Kirchoff’s voltage law is the most accurate?
The sum of the voltage drops in a closed circuit is equal to the applied voltage.
The algebraic sum of the voltage drops in a closed circuit is equal to the applied voltage.
The algebraic sum of the voltage drops in a parallel circuit is equal to the applied voltage.
Notes: MCQ
Correct answer: b
Feedback:
Correct – Well done. That is correct
Incorrect – That is not correct. Kirchoff’s voltage law does not only apply to parallel circuits and it is the not just the sum but the algebraic sum of voltage drops that equals the applied voltage. In other words, if there are 2 voltage drops in a circuit of 2V and -0.5V, this would equate to an applied voltage of 1.5V and not 2.5V.

## Slide 14: Question 3
Indicate whether the following statement is TRUE or FALSE:
Kirchoff’s current law states that the algebraic sum of the currents entering a point is equal to the algebraic sum of the current leaving a point.
True
False
Notes: T/F question
Correct answer: True
Feedback:
Correct – Well done. This is correct.
Incorrect – That is not correct. This statememt is a statement of Kichoff’s first or current law.

## Slide 15: Question 4
Use Kirchoff’s method to calculate the current flow I1 – I2 in this circuit. Enter your answer (correct to 3 decimal places) in the space below. Make sure to include the correct units.
Notes: Maths cloze question with symbol selector
Correct answer: -0.076A or -76mA
See 01_03_04_Activity Solutions for full worked solution.

## Slide 16: Question 5
Study the circuit and then use Kirchoff’s laws to answer the questions that follow:

## Slide 17: Question 5
5.1:
What is the equation of loop ABCEFA?
Notes: MCQ:
Correct answer: c
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_04_Activity Solutions for full worked solution.

## Slide 18: Question 5
5.2:
What is the equation of loop CDEC?
Notes: MCQ:
Correct answer: d
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_04_Activity Solutions for full worked solution.

## Slide 19: Question 5
5.3:
Calculate the value of I1 and I2 and enter your answers (correct to 3 decimal places) in the spaces below. Make sure to include the correct units.
I1
I2
Notes: Maths cloze question with symbol selector
Correct Answer: I1 = 0.624A or 624mA; I2 = 0.047A or 47mA
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_04_Activity Solutions for full worked solution.

## Slide 20: Question 6
Determine the currents I1, I2, I3 and I4 in this circuit making use of Kirchoff’s laws. enter your answers (correct to 3 decimal places) in the spaces below. Make sure to include the correct units.
2,5 A
0,6 A
0,9 A
2,5 A
0,6 A
I1
I2
I3
0,3 A
0,3 A
I4
I1
I2
I3
I4
Notes: Maths cloze question with symbol selector
Correct Answer: I1 = 1.5A; I2 = 1A; I3 = 1.9A; I4 = 0.6A
Feedback:
Correct: Well done. That is correct.
Incorrect. That is not correct. Have a look at the worked solution to see where you went wrong. See 01_03_04_Activity Solutions for full worked solution.

## Slide 21: Video Briefing – Vid01 (1 of 6)
Create a screencast video presented by an expert presenter. The presenter needs to work through the example using Img03 and the following steps. At each step, learners should be encouraged to pause the video and add to their diagram or try the calculations themselves.
Step 1: Label each corner and intersection
VT=24V
R1=6Ω
R2=8Ω
R3=12Ω
R4=4Ω
A
B
C
D
E
F

## Slide 22: Video Briefing – Vid01 (2 of 6)
Step 2: Use KCL to label current in each branch limiting the number of variables to 2. Explain that we could either use I2 = IT – I3 or I3 = IT – I2.
VT=24V
IT
R1=6Ω
R2=8Ω
R3=12Ω
R4=4Ω
I3
I2=I1-I3
A
B
C
D
E
F

## Slide 23: Video Briefing – Vid01 (3 of 6)
Step 3: Choose a CLOSED loop in direction of conventional current. Explain that we could also use loop BCDEB.
VT=24V
IT
R1=6Ω
R2=8Ω
I2=I1-I3
A
B
E
F

## Slide 24: Video Briefing – Vid01 (4 of 6)
Step 4: Use KVL to generate an equation of the voltage drops in the loop.
VT=24V
IT
R1=6Ω
R2=8Ω
I2=I1-I3
A
B
E
F
V1
V2

## Slide 25: Video Briefing – Vid01 (5 of 6)
Step 5: Now set up a similar voltage equation using KVL in the other loop BCDEB.
R2=8Ω
R3=12Ω
R4=4Ω
I3
I2=I1-I3
B
C
D
E
V2
V2
V4
VT = V3 + V4 – V2
VT = 0 since there is no voltage source in the loop.
V2 is negative because the direction of the loop is against the flow of conventional current.
0 = I3R3 + I3R4 – (IT – I3)R2
0 = 12I3 + 4I3 – 8IT + 8I3
0 = 24I3 – 8IT

## Slide 26: Video Briefing – Vid01 (6 of 6)
Step 6: Solve the 2 equations simultaneously
24 = 14IT – 8I3 …. (1)
0 = 24I3 – 8IT …. (2)
Multiply (1) by 3: 72 = 42IT – 24I3
∴ 24I3 = 42IT – 72 … (3)
Substitute (3) into (2): 0 = (42IT – 72) – 8IT
∴ 0 = 42IT – 72 – 8IT = 34IT – 72
∴ 72 = 34IT
∴ IT = 72/34 = 2.118A
Substitute into (3): 24I3 = 42(2.118A) – 72
∴ 24I3 = 16.956A
∴ I3 = 16.956/24 = 0.7065A
∴ I2 = 2.118A – 0.7065A = 1.412A
Check solution with http://everycircuit.com/circuit/5278768561389568

## Slide 27: Video Briefing – Vid02 (1 of 4)
Create a screencast video presented by an expert presenter. The presenter needs to work through the example using Img04 and the following steps. At each step, learners should be encouraged to pause the video and add to their diagram or try the calculations themselves.
Step 1: Redraw the circuit diagram including all the given information. Highlight the 2 loops.
VT=12V
4Ω
I1
I2
8Ω
6Ω
8Ω
2Ω
4Ω
0.9A
I2 - 0.9A
I1 - 0.9A
I1 – I2
D
A
B
C

## Slide 28: Video Briefing – Vid02 (2 of 4)
Work in loop DACD to set up an equation using KVL

## Slide 29: Video Briefing – Vid02 (2 of 4)
Work in loop DABCD to set up an equation using KVL

## Slide 30: Video Briefing – Vid02 (2 of 4)
Solve the equations simultaneously

## Slide 31: Video Briefing – Vid03 (1 of 4)
Create a screencast video presented by an expert presenter. The presenter needs to work through the example using Img05 and the following steps. At each step, learners should be encouraged to pause the video and add to their diagram or try the calculations themselves.
Step 1: Redraw the circuit diagram including all the given information. Highlight the 2 loops.
A
B
C
D
VT=12V
R1=10Ω
R2=15Ω
R3=20Ω
R4=25Ω
R5=5Ω
IT
I1
I2
0.012A
I2+0.012A
I1-0.012A

## Slide 32: Video Briefing – Vid03 (2 of 4)
Work in loop ABDA
VT = V1 + V5 – V4
Remind learners:
VT = 0 because there is no voltage source in the loop
V4 is negative because direction of the loop is opposite to conventional current

## Slide 33: Video Briefing – Vid03 (3 of 4)
Work in loop BCDB
VT = V2 - V3 – V5
Remind learners:
VT = 0 because there is no voltage source in the loop
V3 and V5 are negative because direction of the loop is opposite to conventional current

## Slide 34: Video Briefing – Vid03 (4 of 4)
Solve the equations simultaneously

## Slide 35: Document Briefing – Doc01
Create a worksheet based on 01_03_04_Activity and a worked solutions memo based on 01_03_04_Activity Solutions

## Slide 36
Determine, with the aid of Kirchoff’s laws:
The equation for loop ABDA;
The equation for loop BCDB; and
I1 and I2