## Slide 1: Electrical Principles
Topic 4: Solving AC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Define what alternating current (AC) is
Identify the waveform of AC
Explain why AC is used for electrical distribution systems
Explain how a simple AC generator works
Explain what the peak value, RMS and average value for AC voltage and current are and how they are calculated.

## Slide 4: Unit 4.1: Alternating Current

## Slide 5: Introduction
This topic is all about AC (Alternating Current) and how it is different to DC (Direct Current).
The differences between AC and DC are expressed very nicely in their symbols, as we shall see.
Click on each symbol to see a simple definition of each type of electricity.
Notes: Img01 = DC and AC symbols
DC = on click, open slide 7 in a popup
AC = on click, open slide 8 in a popup
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Direct Current
Direct current or DC is the kind of electricity you get out of batteries. It is at a fixed voltage and the electrons always flow in the same direction.
Vid01
Notes: Vid01 = DC animation similar to that found at https://www.youtube.com/watch?v=JZjMuIHoBeg
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 7: Alternating Current
Alternating current or AC is the kind of electricity that comes out of your plug. The electrons do not always flow in the same direction. They keep changing or alternating direction.
Vid02
Notes: Vid02 = AC animation similar to that found at https://www.youtube.com/watch?v=JZjMuIHoBeg
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 8: What is alternating current
So we have seen that AC stands for alternating current – current where the direction of the electrons keeps changing. In other words, they move back and forth.
Vid03
Watch this video to find out more.
Notes: Vid03 = on click, play Vid03 full screen. See appendix for brief.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Representing DC
We can represent the voltage and current of a circuit against time with a graph.
Here is a typical DC graph. The voltage and current are constant. Because the voltage is always positive, current always flows in the same direction.
Click on the image to see a larger version.
Img02
Notes: Img02 = on click, display Img02 full screen. Img02 based on https://www.desmos.com/calculator/pbgqwemstz – redraw and label orange line current and purple line voltage. Also add in + and – labels for the y-axis.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: Representing AC
Here is a typical AC graph. The voltage and current are not constant. Because the voltage changes polarity (goes from positive to negative), the current flows in one direction (indicated as positive) and then the other direction (indicated as negative). It alternates.
Click on the image to see a larger version.
Img03
Notes: Img03 = on click, display Img03 full screen. Img03 based on https://www.desmos.com/calculator/l6xrii16lm – redraw and label orange line current and purple line voltage. Also add in + and – labels for the y-axis.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 11: Pulsating DC
Sometimes the voltage of DC is not constant. However, even in this case, the voltage does not change polarity (change from positive to negative) so, even though the amount of current changes, it NEVER flows in the opposite direction. It always still flows in ONE direction. This is called pulsating DC.
Click on the image to see a larger version.
Img04
Notes: Img04 = on click, display Img04 full screen. Img04 based on https://www.desmos.com/calculator/5nn2hx3tlj – redraw and label orange line current and purple line voltage. Also add in + and – labels for the y-axis.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 12: Question 1
Which of the following graphs represent AC?
Img05
Img06
Img07
Img08
a)
b)
c)
d)
Notes: Img05 = https://www.desmos.com/calculator/g8shvgobii – red line
Img06 = https://www.desmos.com/calculator/g8shvgobii – purple line
Img07 = https://www.desmos.com/calculator/g8shvgobii – blue line
Img08 = https://www.desmos.com/calculator/g8shvgobii – orange line
Multiple choice question
Correct answer: d
Feedback:
A – That is not correct. This graph represents typical constant voltage DC.
B - That is not correct. This graph represents pulsating DC. The voltage is always positive so current will always flow in the same direction.
C – That is not correct. This graph represents pulsating DC. The voltage is never negative. Times when the voltage is zero, represent when no current will flow, but the polarity is never reversed so current will never flow in the other direction.
D – Well done! This graph represents typical AC.

## Slide 13: Question 2
Which graphs represents AC?
1 only
2 only
1 and 2
Neither
Img09
Img10
1)
2)
Notes: Img09 = https://www.desmos.com/calculator/v0q9fnx2qj – orange line
Img10 = https://www.desmos.com/calculator/v0q9fnx2qj – purple line
Multiple choice question
Correct answer: a
Feedback:
A – Well done. Graph 1 represents AC because, for some of the time, the voltage is positive and it then becomes negative. This means the polarity switches so current will flow in the other direction.
B – That is not correct. Graph 2 is DC. Even though the voltage is shown as negative, it never changes to become positive so the polarity does not change. Therefore, current does not flow in the other direction ever.
C – That is not correct. Graph 1 does represents AC because, for some of the time, the voltage is positive and it then becomes negative. This means the polarity switches so current will flow in the other direction. But graph 2 does not represent AC. Even though the voltage is shown as negative, it never changes to become positive so the polarity does not change. Therefore, current does not flow in the other direction ever.
D – That is not correct. Graph 1 does represents AC because, for some of the time, the voltage is positive and it then becomes negative. This means the polarity switches so current will flow in the other direction.

## Slide 14: Question 3
Which of the following graphs represent DC?
1 only
1 and 3
1 and 2
None
Img11
Img12
Img13
Img14
1)
2)
3)
4)
Notes: Img11 = https://www.desmos.com/calculator/4oowoiewmw – red line
Img12 = https://www.desmos.com/calculator/4oowoiewmw – green line
Img13 = https://www.desmos.com/calculator/4oowoiewmw – blue line
Img14 = https://www.desmos.com/calculator/4oowoiewmw – orange line
Multiple choice question
Correct answer: b
Feedback:
A – That is not correct. While graph 1 does represent DC (the voltage is never negative so current always flows in the same direction), graph 3 also represents DC.
B – Well done. Both graphs 1 and 3 always have positive voltage so the current always flows in the same direction.
C – That is not correct. While graph 1 does represent DC (the voltage is never negative so current always flows in the same direction), graph 2 has negative voltage. This means that the polarity is reversed and current will flow in the opposite direction i.e. AC.
D – That is not correct. Graphs 2 and 4 have periods where the voltage is negative. During these times, the polarity will be reversed and current will flow in the opposite direction. Graphs 1 and 3 never have negative voltage so the polarity is never reversed. Therefore, these represent DC as direct only ever flows in one direction.

## Slide 15: Why bother with AC?
Watch this video to learn the story behind why we use AC today.
So many of our household appliances need DC, not AC to run. So why do we bother with AC at all?
The answer has to do with how electricity gets to our homes in the first place.
YT01
Notes: YT01 = on click, play YT01 full screen. YT01 = https://www.youtube.com/watch?v=xyQfrzBfnDU
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 16: Why AC
Click on each box to unpack each part of the argument.
Efficiency
The need to get energy from the power station to your home.
Safety
The need to make the delivery of electricity safe.
1
2
There are two parts to the argument for distributing electricity as AC.
Notes: Power = on click, present slide 18 as a popup
Transformers = on click, present slide 19 as a popup
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 17: Efficiency
Higher voltages mean less current for the same power.
Less current means smaller energy losses.
1
2
Less current means thinner/cheaper cables.
3
We have to get electrical energy or power from the power station to your home. Power = voltage x current.
We distribute power at high voltages.
4
Less current means thinner/cheaper cables.
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 18: Safety
We distribute power at high voltages.
High voltage in homes is dangerous
1
2
We use transformers to change the voltage.
3
We have to get electrical energy to your home safely and in a safe to use format.
Transformers only work with AC.
4
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 19: Write your own explanation
In the space provided, write your own explanation for why we distribute electrical energy (or power) as AC. This will become part of your online portfolio.
Submit
Notes: Paragraph question. On submission, present the following response and model answer. “You said [response text]. The equation P = I x V tells us that, if we distribute power at higher voltages, we reduce the current in the wires for the same power. Reducing the current, means that we can use thinner and less expensive wires. Reducing the current also means that we reduce the losses because of resistance. The equation P = I2 x R tells us that the relationship between power and current is exponential, meaning that reducing the current a bit, reduces the losses a lot.
But delivering high voltage to people’s homes is dangerous so we need a way to reduce the voltage. Transformers are machines that do this well but they only work with AC. For this reason, we distribute electrical energy or power as AC.
Submit = submit text.

## Slide 20: Generating AC
Click the button if you need to revise electromagnetism form topic 2.
Most power stations around the world generate AC power using AC generators (also called alternators). Generators convert kinetic energy into electrical.
To understand how they work, you need to understand the basics of electromagnetism.
Revise electromagnetism
Notes: Img15 = https://upload.wikimedia.org/wikipedia/commons/a/a6/93-01-xx%2C_Zimmer_Power_Plant%2C_Generator_and_Turbine.jpg – marked for reuse
Revise electromagnetism = on click, open 01_02_01
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 21: Electromagnetic induction
Click the button to watch a great video of how AC generators work.
The two basic principles of electromagnetic induction explain how an AC generator works.
When a conductor is placed inside a changing magnetic field, an emf is induced in the conductor.
The size of the induced emf is proportion to the rate of change of the magnetic field.
1
2
Electromagnetic induction
Notes: Electromagnetic induction = on click, play YT02 full screen. YT02 = https://www.youtube.com/watch?v=jeTmIa00_rc
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 22: Basic principles
From the previous video, we learnt some very important things.
Electromagnetic induction is produced in a conductor by a change in magnetic flux.
Magnetic flux = the strength of the magnetic field x surface area of the conductor perpendicular to the magnetic field.
1
2
If we spin a magnet near a wire, the wire will experience a constantly changing magnetic flux and an AC current will be induced.
3
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 23: Real AC generators
Watch the video for a detailed look at how real AC generators work.
Most of the time, it is not the magnet that spins near a coil of wire. Rather, a coil of wire is turned inside a magnetic field.
YT03
Notes: YT03 = on click, play YT03 full screen. YT03 = https://www.youtube.com/watch?v=gQyamjPrw-U
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 24: How much emf is induced?
Click on each symbol to learn what it means.
The amount of of emf induced (or current produced) by a generator is given by the following equation.
Notes: E = on click, present the following in a popup – “This is the induced emf or voltage (measured in V).”
Beta = on click, present the following in a popup = “This is the Greek letter beta and is the strength or density of the magnetic flux (measured in Teslas). We can increase the emf by using stronger magnets.”
L = on click, present the following in a popup = “This is the length of the conductor or wire inside the generator (measured in metres). We can increase the emf by using more wire.”
v = on click, present the following in a popup = “This is the velocity with which the conductor is moving (measured in metres/second). We can increase the emf by spinning the conductor faster.”
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 25: Ste by step
Click on the button to rotate the conductor step-by-step through the magnetic field to see the result.
Img16
Notes: Img16 = See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 26: How much emf is induced?
Drag the following descriptions of what is happening in an AC generator to the correct picture.
Maximum emf is induced.
No emf is induced
Some emf is induced
N
S
Some emf is induced but in the opposite direction
N
S
Notes: Drag and drop question:
Top picture = part 8 of Img16 – Maximum emf is induced
Bottom picture = part 5 of Img16 – Some emf induced but in the opposite direction
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 27: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you understand resistors in series.
Notes: Tanya to provide

## Slide 28: Video Briefing – Vid03 (1 of 3)
Create a screencast video presented by an expert presenter. Use the Phet Circuit Construction Kit (AC+DC), available at https://phet.colorado.edu/en/simulation/circuit-construction-kit-ac, to explain the difference between AC and DC.
Create a simple DC circuit with a battery and light bulb
  Show how the electrons always flow in one direction from negative to positive
  Explain that conventional current therefore also always flows in one direction, from positive to negative
Create a simple AC circuit with a AC source and light bulb next to the DC circuit
  Emphasise how the electrons keep switching direction
  Explain how this change in direction makes the bulb go on and off (you can lower the frequency to make this clearer)
    Current starts to flow in one direction and the bulb lights up
    Current then starts to slow down in this direction and the bulb starts to dim
    At some point, the electrons stop (no current flowing) and the bulb is off
    Then electrons start flowing in the opposite direction and the bulb gets brighter again
    Current then starts to slow down in this direction and the bulb starts to dim

## Slide 29: Video Briefing – Vid03 (2 of 3)
Add voltage and current meters to both circuits to show
  How the current in DC is constant
  How the voltage in DC is constant
  How the current in AC is always changing
  How the voltage in AC is always changing
Draw the link between how (you can pause the animation to make the following points)
  When the voltage is increasing to a positive maximum, the current increases to a positive maximum (we know that with constant R, when voltage increases, current increases)
  When the voltage decreases to zero, the current decreases to zero
  When the voltage is zero, the current is zero
  When the voltage goes below zero or becomes negative, this means the polarity of the supply has changed – the positive and negative terminals are switched around.
  As voltage becomes negative and the polarity is switched, current starts to flow in the opposite direction. If the negative terminal is on the other side of the supply, then this side of the supply will start to push the electrons

## Slide 30: Video Briefing – Vid03 (3 of 3)
  As voltage increases to a negative maximum, the current increases but is shown as negative because it is in the other direction.
  When voltage gets to its negative maximum, current is at its maximum
  As voltage starts to decrease back to zero, current starts to decrease back to zero.
  See https://www.dropbox.com/s/avcunvjy7cwe9lk/AC%20vs%20DC?dl=0 for an example of the Phet animation setup

## Slide 31: Image Briefing – Img16 (1 of 10)
Create a set of images that are displayed one by one as the learner clicks on the button. This is the basic design of the images.
Next
N
S

## Slide 32: Image Briefing – Img16 (2 of 10)
Position 1
N
S
Next
Conductor at 0°
The conductor lies parallel to the magnetic field lines and is no cutting any of the field lines. Therefore, no emf is induced in the conductor.

## Slide 33: Image Briefing – Img16 (3 of 10)
Position 2
Next
Conductor at 45°
The conductor cuts the field lines and its magnetic flux is increasing. Therefore, an emf is induced and current flows in the positive direction.
N
S

## Slide 34: Image Briefing – Img16 (4 of 10)
Position 3
N
S
Next
Conductor at 90°
The conductor is perpendicular to the field lines. Its magnetic flux is at a maximum. Therefore a maximum emf is induced.

## Slide 35: Image Briefing – Img16 (5 of 10)
Position 4
N
S
Next
Conductor at 135°
The conductor is now cutting fewer field lines. Its magnetic flux is decreasing and a smaller emf then before is being produced.

## Slide 36: Image Briefing – Img16 (6 of 10)
Position 5
N
S
Next
Conductor at 180°
The conductor is once again parallel to the field lines. Therefore there is no magnetic flux and no emf is induced.

## Slide 37: Image Briefing – Img16 (7 of 10)
Position 6
Next
Conductor at 225°
The conductor cuts the field lines and an emf is produced. This time, however, the other side of the conductor is facing the North pole. Therefore the induced emf is reversed and current will flow in the opposite direction to before.
N
S

## Slide 38: Image Briefing – Img16 (8 of 10)
Position 7
Next
Conductor at 270°
The conductor is again perpendicular to the field lines so magnetic flux is a maximum. Therefore a maximum emf is induced, but this time in the opposite direction to before.
N
S

## Slide 39: Image Briefing – Img16 (9 of 10)
Position 8
Next
Conductor at 315°
The conductor is cutting fewer field lines then before so the magnetic flux has reduced. Therefore the induced emf has also reduced.
N
S

## Slide 40: Image Briefing – Img16 (10 of 10)
Position 9
Next
Conductor at 360°
The conductor has rotated through a full cycle and again lies parallel to the field lines. Therefore, no emf is induced.
N
S