## Slide 1: Electrical Principles
Topic 4: Solving AC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Calculate resistance, inductive reactance, impedance, voltage, current, power, power factor and frequency in a series RC circuit.
Construct a phasor diagram to represent the relationship between the voltage and current in a series RC circuit.

## Slide 4: Unit 4.5: Series RC Circuits

## Slide 5: Introduction
In the previous unit we learnt how to work with AC circuits that had resistors and inductors in them.
In this unit, we are going to look at how circuits with resistors and capacitors in them behave.
Notes: Img01 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Series RC circuits
We know that series circuits have all the components connected end to end so that there is only one path for the current. Let’s investigate what happens when we have a resistor and a capacitor together in a series circuit.
Download and work through the worksheet. Then watch the video to make sure you completed everything correctly.
Download the worksheet
Vid01
Notes: Download the worksheet = on click, open Doc01. See appendix for brief
Img02 = EveryCircuit logo
Vid01 = on click, play Vid01 full screen. See appendix for brief

## Slide 7: Series RC Circuits
In series AC circuits where there are resistors and capacitors, we need to take account of the fact that the voltage across the capacitor lags the current through the capacitor by 90° when doing calculations.
The voltage across and current through the resistor are in phase.
A series RC circuit
V and I
waveforms
VR
IT
VC
Notes: Img03 = Img01 + label
Img04 = redraw graphs
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 8: Total voltage in a series RC circuit
The total voltage drop in a series RC circuit is the vector sum of the voltage drops across the resistor and the capacitor. Remember that Kirchoff’s Voltage Law does not work.
Phasor Diagram
θ
VC -90°
VR 0°
VT θ
IT
Notes: Img05 = Redraw the phasor diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Total impedance in series RC circuits
The combined resistance to the flow of current from resistance and reactance is called impedance (Z). It is measured in Ω. The total impedance in a series RC circuit is the vector sum of the resistance and capacitive reactance.
VR
(R)
VC
(XC)
VT
(Z)
Phasor Diagram
VC
(XC)
θ
Notes: Img06 = redraw the phasor diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: The phase angle in series RC circuits
There are many ways to calculate the phase angle (θ) in a series RL circuit.
θ
VC -90°
VR 0°
VT θ
VR
(R)
VC
(XC)
VT
(Z)
VC
(XC)
θ
Notes: Img07 = based on Img05
Img08 = based on Img06
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 11: Power in series RC circuits
The current in this circuit leads the voltage by the phase angle, θ, because of the capacitor. Therefore the circuit has a leading power factor.
(lagging)
P = true power (W)
VT = total voltage (V)
IT = total current (A)
θ = phase angle (°)
Notes: Img07 = based on Img05
Img08 = based on Img06
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 12: Solving series RL circuits – example 1
Let’s start with this example.
Redraw the circuit on a blank piece of paper.
The capacitance of the capacitor is unknown. Calculate the:
Impedance;
The reactance
Value of the capacitor;
Voltage across each component;
Phase angle; and
Draw the phasor diagram.
200V
IT = 10.6A
Notes: Img09 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 13: Solving series RC circuits – step 1
Remember that this is still a series circuit so IT = IR = IC.
Once you have drawn the basic circuit, you need to label it. When dealing with series RC circuits, it is important that you label it correctly. This will help later on.
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10 = redraw circuit diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 14: Solving series RC circuits – step 2
Now we can start answering the questions.
Calculate the total impedance in the circuit. Enter your answer to three decimal places.
Check
Ω
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10
Fill in the blank question
Correct answer: 18.868Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 15: Solving series RC circuits – step 2
Calculate the reactance in the circuit. Enter your answer to three decimal places.
Check
Ω
XC
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10
Fill in the blank question
Correct answer: XC = 16.000Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 16: Solving series RC circuits – step 2
Calculate the capacitance of the capacitor. Enter your answer to 1 decimal place
Check
C
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
μF
Notes: Img10
Fill in the blank question
Correct answer: C = 198.9μF
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that . If you are struggling to do this calculation on your calculator, be sure to watch the full worked solution video at the end of this example.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 17: Solving series RC circuits – step 2
Calculate the voltage drop across each component. Enter your answers to one decimal place.
Check
V
VR
V
VC
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10
Fill in the blank question
Correct answer: VR = 106.0V, VL = 169.6V
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that IT = IR = IL. So VR = IT x R = 10.6 x 10 = 160V. VC = IT x XC = 10.6 x 16 = 169.6V
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 18: Solving series RC circuits – step 2
Calculate the phase angle. Enter your answer to three decimal places.
Check
θ
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10
Fill in the blank question
Correct answer: θ = 57.995°
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. Cosθ = R/Z= 10/18.868. Therefore θ = 57.995°
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 19: Solving series RC circuits – step 2
Draw the phasor diagram for this circuit on a piece of paper then take a photo of it and upload it to your online portfolio.
Choose image
Upload
Notes: Img11 = https://cdn.pixabay.com/photo/2016/01/03/00/43/upload-1118929_960_720.png – marked for reuse
Choose image = Launch file selection window
Upload = Upload file
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 20: Solving series RC circuits - solution
Watch the video to see the full worked solution for this question.
You can also have a look at a simulation of the circuit.
Full worked solution
See the circuit simulation
IT = 10.6A
VT = 200V
R =
C = ?
IR
IC
VR
VC
Notes: Img10
Full worked solution = on click, open Vid03 full screen. See appendix for brief.
See the circuit simulation = on click, open http://everycircuit.com/circuit/6566729630351360 in a new window
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 21: Solving series RC circuits – example 2
Full worked solution
In this circuit, calculate the:
Impedance;
Capacitive reactance;
The frequency of the supply;
True power;
Power factor; and
Draw the phasor diagram
Try the question on your own and then watch the full worked solution.
Circuit simulation
90V
IT = 818mA
Notes: Img11 – redraw circuit
Full worked solution = on click, play Vid03 full screen. See appendix for brief
Circuit simulation = on click, open http://everycircuit.com/circuit/6134386931269632 in a new window
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 22: Document Briefing – Doc01 (1 of 2)
Create an annotated PDF worksheet with the following steps.
Make sure you have downloaded the EveryCircuit App from your app store.
If you are working on a computer, visit http://everycircuit.com/app/.
Open the EveryCircuit app and signup. After your trial, you will still have access to EveryCircuit and other people’s circuits. You will just not be able to create your own circuits.
Go to the community space and search for the circuit called “NOC_Series RC Circuit”
Open the circuit.
This circuit has an AC power supply with a frequency of 1kHz (or 1 000 cycles per second) and a peak voltage of 9V. It also has a 470Ω and a 1μF capacitor.
Click on the ammeter to find out what its reading is. Is this the same current through the resistor and the capacitor? Why or why not?
We know that the capacitance (XC) of a capacitor is given by . Calculate XC.
Now calculate the voltage across the capacitor, VC.
Calculate the voltage across the resistor VR.

## Slide 23: Document Briefing – Doc01 (2 of 2)
Use the knowledge you gained from RL circuits, to see if we calculate VT in RC circuits the same way i.e. is
We know that impedance (Z) is the sum of all the resistance and reactance in a circuit. Use VT and IT to calculate the total impedance in the circuit.
Now calculate the total impedance in the circuit using the resistance R and the capacitive reactance of XC the same way we did for RL circuits i.e. using . Do you get the same answer for Z as before?
Try and draw the phasor for this circuit. In this case does voltage LEAD or LAG the current?
Calculate the phase angle in this circuit.

## Slide 24: Video Briefing – Vid01 (1 of 2)
Create a screencast video presented by an expert presenter. The presenter needs to work through the Doc01 worksheet and cover and explain the following steps.
Opening the app and opening the circuit for mobile and desktop
Calculate XC, VC and VR.
Check that VL and VR are the same as the voltmeter readings in the simulation.
Show that VT can be calculated using the same method as with RL circuits i.e. using vector addition
  Note that this time the voltage across the capacitor LAGS the current by 90° – show this by displaying the voltage across the capacitor on the graph.
  Draw the phasor diagram with and
  Do the vector addition graphically (1cm = 1V) and then algebraically.
Calculate the total Z using V / IT
Calculate Z using .
VC -90°V
VR 0° V

## Slide 25: Video Briefing – Vid01 (2 of 2)
Show that the answers are the same.
Explain that we deal with series RC circuits the same way as series RL except that the phasor is different because voltage LAGS current by 90°
Calculate the phase angle
  Use and reminding people (using the phasor) that any of the 6 methods will work.

## Slide 26: Video Briefing – Vid02 (1 of 3)
Create a screencast video presented by an expert presenter. The presenter needs to work through the question in example 1.
The capacitance of the capacitor is unknown. Calculate the:
Impedance;
The reactance
Value of the capacitor;
Voltage across each component;
Phase angle; and
Draw the phasor diagram.
200V
IT = 10.6A

## Slide 27: Video Briefing – Vid02 (2 of 3)

## Slide 28: Video Briefing – Vid02 (3 of 3)

## Slide 29: Video Briefing – Vid03 (1 of 5)
Create a screencast video presented by an expert presenter. The presenter needs to work through the question in example 2.
In this circuit, calculate the:
Impedance;
Capacitive reactance;
The frequency of the supply;
True power;
Power factor; and
Draw the phasor diagram
90V
IT = 818mA

## Slide 30: Video Briefing – Vid03 (2 of 5)
IT = 818mA
Redraw and label the circuit as follows. Note that IT = IR1 = IR2 = IC
VT = 90V
R1 =
R2 =
IR1
VC
VR1
VR2
C =
IC
IR2

## Slide 31: Video Briefing – Vid03 (3 of 5)
Question 1:
Z = VT / IT = 90V / 0.189A = 476.190Ω
Question 2:
Total series resistance = 20Ω + 90Ω = 110Ω
Question 3:

## Slide 32: Video Briefing – Vid03 (4 of 5)
Question 4:
True power P = VIcosθ. But cosθ = R / Z = 110 / 476.190. Therefore θ = 76.644°
So P = 90V x 0.189 x cos(76.644) = 3.929W
Question 5:
Power factor = cosθ = cos76.644° = 0.231

## Slide 33: Video Briefing – Vid03 (5 of 5)
Question 6:
RT = 110Ω
XC = 463.311Ω
Z = 476.190Ω
76.644°
Draw the phasor with impedance as XL and RT were known. Had not worked out voltage drop across both resistors.