## Slide 1: Electrical Principles
Topic 4: Solving AC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Calculate resistance, inductive reactance, impedance, voltage, current, power, power factor and frequency in a series RLC circuit.
Construct a phasor diagram to represent the relationship between the voltage and current in a series RLC circuit.

## Slide 4: Unit 4.6: Series RLC Circuits

## Slide 5: Introduction
In the previous two units we have looked at RL and RC circuits. But what happens when we have resistors, inductors AND capacitors all together in the same circuit?
Well, in this unit, we will find out.
Notes: Img01 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Summary of RL and RC circuits
Let’s revise some of what we know about series RL and RC circuits.
Series RL Circuits
Series RC Circuits

## Slide 7: RL + RC circuits = RLC circuits
But what happens when we put series RL and RC circuits together.
Waveforms
Phasor Diagrams
Vid01
Vid02
Click on each animation to watch it.
Notes: Vid01 = on click, play Vid01 full screen. See appendix for brief.
Vid02 = on click, play Vid02 full screen. See appendix for brief.

## Slide 8: The basics of solving series RLC circuits
We just saw that if VL = VC in a RLC circuit, they will cancel each other out and the circuit behaves as if it only has resistors i.e. where the voltage is in phase with the current.
But usually VL and VC are not the same and the voltage either leads or lags the current.
Vid03
Watch the video to see how to deal with RLC circuits where VL and VC are different.
Notes: Img03 = Img01 + label
Img04 = redraw graphs
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Series RLC circuits where XL > XC
When XL > XC, the circuit behaves inductively and, therefore overall, voltage LEADS current.
VR
(R)
VL – VC
(XL – XC)
VT
(Z)
θ
Phasor Diagram
IT
VL
(XL)
VC
(XC)
Notes: Img02 = Redraw the phasor diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: Series RLC circuits where XC > XL
When XC > XL, the circuit behaves capacitively and, therefore overall, voltage LAGS current.
VR
(R)
VC – VL
(XC – XL)
VT
(Z)
θ
Phasor Diagram
IT
VL
(XL)
VC
(XC)
Notes: Img03 = Redraw the phasor diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 11: The phase angles in series RLC circuits
There are many ways to calculate the phase angle (θ) in a series RLC circuit.
Click on each image to see a larger version.
Img04
Img05
Notes: Img04 = on click, open Img04 in a popup. See appendix for brief
Img05 = on click, open Img05 in a popup. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 12: Which is which?
Here’s a good way to remember in which situation the voltage leads or lags the current.
CIVIL
In a capacitive circuit (C)
I LEADS V
In an inductive circuit (L)
V LEADS I
Notes: Img06 = CIVIL plus borders, arrows and labels
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 13: Solving series RLC circuits – example 1
Let’s put all our new knowledge to work with an example.
Redraw the circuit on a blank piece of paper.
Calculate the:
Impedance;
Total current;
Inductance of the inductor;
Capacitance of the capacitor;
Phase angle; and
Draw the phasor diagram.
40Ω
60Ω
VT = 230V
Notes: Img07 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 14: Solving series RLC circuits – step 1
Remember that this is still a series circuit so IT = IR = IL=IC
Once you have drawn the basic circuit, you need to label it. When dealing with series RLC circuits, it is important that you label it correctly. This will help later on.
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08 = redraw circuit diagram
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 15: Solving series RLC circuits – step 2
Now we can start answering the questions.
Calculate the total impedance in the circuit. Enter your answer to three decimal places.
Check
Ω
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08
Fill in the blank question
Correct answer: 53.852Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We do not know the total circuit current yet so we cannot use to calculate the total impedance. But we do know the resistance and reactance of the various components. We also know that XC > XL so we can calculate impedance as follows:
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 16: Solving series RLC circuits – step 2
Calculate the total circuit current. Enter your answer to three decimal places.
Check
A
IT
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08
Fill in the blank question
Correct answer: IT = 4.523A
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know the total voltage and the total impedance. Therefore we can calculate total current as
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 17: Solving series RLC circuits – step 2
Calculate the inductance of the inductor. Enter your answer to 2 decimal place.
Check
L
mH
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08
Fill in the blank question
Correct answer: L = 127.32mH
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that .
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 18: Solving series RLC circuits – step 2
Calculate the capacitance of the capacitor. Enter your answer to 1 decimal place
Check
C
μF
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08
Fill in the blank question
Correct answer: C = 53.051μF
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that . If you are struggling to do this calculation on your calculator, be sure to watch the full worked solution video at the end of this example.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 19: Solving series RLC circuits – step 2
Calculate the phase angle. Enter your answer to three decimal places.
Check
θ
°
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img08
Fill in the blank question
Correct answer: θ = 21.802°
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct.. Therefore θ = 21.802°
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 20: Solving series RLC circuits – step 2
Draw the phasor diagram for this circuit on a piece of paper then take a photo of it and upload it to your online portfolio.
Choose image
Upload
Notes: Img09 = https://cdn.pixabay.com/photo/2016/01/03/00/43/upload-1118929_960_720.png – marked for reuse
Choose image = Launch file selection window
Upload = Upload file
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 21: Solving series RLC circuits - solution
Watch the video to see the full worked solution for this question.
You can also have a look at a simulation of the circuit.
Full worked solution
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC
Notes: Img10
Full worked solution = on click, open Vid04 full screen. See appendix for brief.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 22: Solving series RLC circuits – example 2
Full worked solution
Calculate the:
Total voltage;
VC if XC = 3.979Ω;
VL;
Frequency of the supply;
Total impedance; and
Draw the phasor diagram
Try the question on your own and then watch the full worked solution.
A series RLC circuit has a total current of 3.67A. It contains a resistor (75Ω), an inductor (50mH) and a capacitor (125μF). In the circuit XL > XC.
The true power is known to be 1.013kW with a phase angle of 52.161°.
Notes: Img11 – redraw circuit
Full worked solution = on click, play Vid05 full screen. See appendix for brief
Circuit simulation = on click, open http://everycircuit.com/circuit/6134386931269632 in a new window
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 23: Video Briefing – Vid01 (1 of 2)
Create a 2 step animation showing the combining of the RL and RC waveforms into a single graph. On play, slide the 2 graphs towards each other to form the graph in the next slide.
VR
IT
VC
VR
IT
VL
Series RL Circuit
Series RC Circuit
In a series RL circuit, the voltage leads the current.
In a series RC circuit, the voltage lags the current.
Notes: These 2 images are the same as Img04 in 01_04_03 and Img04 in 01_04_04
In the right hand RC diagram, make blue VC line and label orange instead

## Slide 24: Video Briefing – Vid01 (2 of 2)
This is what the final graph must look like. Transition to the new heading and description. Also transition between the initial and final label positions.
Series RLC Circuit
Here VL and VC are out of phase by 180°. If they are the same magnitude, they will cancel each other out.
VR
IT
VL
VC

## Slide 25: Video Briefing – Vid02 (1 of 2)
Create a 2 step animation showing the combining of the RL and RC phasors into a single diagram. On play, slide the 2 graphs towards each other to form the diagram in the next slide.
Series RL Circuit
Series RC Circuit
In a series RL circuit, the voltage leads the current.
In a series RC circuit, the voltage lags the current.
VC -90°
VR 0°
IT
VR 0°
VL 90°
IT
Notes: These 2 images are based on Img05 in 01_04_03 and Img05 in 01_04_04
Note – use the same colours for each variable as in Vid01
In the right hand RC diagram, make blue VC line and label orange instead

## Slide 26: Video Briefing – Vid02 (2 of 2)
This is what the final graph must look like. Transition to the new heading and description. Also transition between the initial and final label positions.
Series RLC Circuit
VR 0°
VL 90°
IT
VC -90°
Here VL and VC are out of phase by 180°. If they are the same magnitude, they will cancel each other out.

## Slide 27: Video Briefing – Vid03 (1 of 3)
Create a screencast video presented by an expert presenter explaining the following:
Start with a phasor where XL > XC (XL = 4Ω, XC = 1.5Ω, R = 6Ω). Let’s assume IT = 2A.
Calculate VL, VC, VR. Add the voltages to the phasor diagram.
In order to do the vector sum, we need to find the combination of VL and VC. They are acting in opposite directions so the result is just VL – VC or 8V - 3V. We always subtract the smaller vector from the larger one.
Draw the new phasor with (VL - VC) and do the vector sum graphically (1V = 1cm) and then algebraically.
Because the voltage drops across the inductor and capacitor are directly proportional to their reactances, we know that if XL > XC then VL > VC and the circuit will behave inductively. In this case, we do the normal vector sum but with the new resulting leading voltage of VL - VC

## Slide 28: Video Briefing – Vid03 (2 of 3)
Now draw a phasor where XC > XL (XL = 4Ω, XC = 7.5Ω, R = 12Ω). Let’s assume IT = 2A.
Calculate VL, VC, VR. Add the voltages to the phasor diagram.
In order to do the vector sum, we need to find the combination of VL and VC. They are acting in opposite directions but now VC > VL so the result is VC – VL or 15V - 8V. Remember, we always subtract the smaller vector from the larger one.
Draw the new phasor with (VC - VL) and do the vector sum graphically (1V = 1cm) and then algebraically.
Because the voltage drops across the inductor and capacitor are directly proportional to their reactances, we know that if XC > XL then VC > VL and the circuit will behave capacitively. In this case, we do the normal vector sum but with the new resulting leading voltage of VC - VL

## Slide 29: Video Briefing – Vid03 (3 of 3)
Now do the case where XC = XL (XL = 5Ω, XC = 5Ω, R = 12Ω). Let’s assume IT = 2A.
Calculate VL, VC, VR. Add the voltages to the phasor diagram.
Because VC = VL they cancel out and the voltage is in phase with the current
Draw the new phasor with (VC = VL)
Because the voltage drops across the inductor and capacitor are directly proportional to their reactances, we know that if XC = XL then VC = VL and the circuit will behave resistively. In this case, we can ignore VC / VL.

## Slide 30: Image Briefing – Img04
VR
(R)
VL – VC
(XL – XC)
VT
(Z)
θ
IT
VL
(XL)
VC
(XC)

## Slide 31: Image Briefing – Img05
VR
(R)
VC – VL
(XC – XL)
VT
(Z)
θ
IT
VL
(XL)
VC
(XC)

## Slide 32: Video Briefing – Vid04 (1 of 3)
Create a screencast video presented by an expert presenter. The presenter needs to work through the question in example 1.
Calculate the:
Impedance;
Total current;
Inductance of the inductor;
Capacitance of the capacitor;
Phase angle; and
Draw the phasor diagram.
XL = 40Ω
XC = 60Ω
VT = 230V
VR
VL
VC
R =
IT
IR
IL
IC

## Slide 33: Video Briefing – Vid04 (2 of 3)

## Slide 34: Video Briefing – Vid04 (3 of 3)

## Slide 35: Video Briefing – Vid05 (1 of 5)
Create a screencast video presented by an expert presenter. The presenter needs to work through the question in example 2.
A series RLC circuit has a total current of 3.67A. It contains a resistor (75Ω), an inductor (50mH) and a capacitor (125μF). In the circuit XL > XC.
The true power is known to be 1.013kW with a phase angle of 52.161°.
Calculate the:
Total voltage;
VC if XC = 3.979Ω;
VL;
Frequency of the supply;
Total impedance; and
Draw the phasor diagram

## Slide 36: Video Briefing – Vid05 (2 of 5)
Start by drawing and labelling the circuit with what is known and unknown. Note that IT = IR = IC = IL
VT
R =
IT = 3.67A
VR
L =
C =
VL
VC
IR
IL
IC

## Slide 37: Video Briefing – Vid05 (3 of 5)
Question 1:
P = VIcosθ; θ = 52.161° and I = 3.67A
V = P / Icosθ = 1013 / 3.67 x cos52.161 = 449.953V ≃ 450V
Question 2:
VC = IT x XC where XC = 3.979Ω
VC = 3.67 x 3.979 = 14.603V
Question 3:
We do not know XL and cannot calculate it without f, so we cannot use VL = IT x XL. We know VR = IT x R = 3.67 x 75 = 275.25V
= = 14.603 =341.399V

## Slide 38: Video Briefing – Vid05 (4 of 5)
Question 4:
We know that XC = 3.979Ω and that C = 125μF so we can calculate f.
XC = 1 / 2πfC
f = 1 / 2πXCC = 1 / 2π x 3.979 x 125 x 10-6 = 320Hz
Question 5:
Z = VT / IT = 450 / 3.67 = 122.615Ω
OR
With f, we can calculate XL.
XL = 2πfL = 2π x 320 x 50 x 10-3 = 100.531Ω
Now we can calculate Z: NOTE: slight difference in answers due to rounding errors.

## Slide 39: Video Briefing – Vid05 (5 of 5)
Question 6:
VT = 275.25V
VL = 341.399Ω
VT = 450V
52.161°
VC = 14.603V
VL – VC = 326.796V