## Slide 1: Electrical Principles
Topic 4: Solving AC Electrical Circuits

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
Explain what the resonant frequency of a series RLC circuit is
Describe the conditions present in a resonant or tuned series RLC circuit
Calculate the resonant frequency for a series RLC circuit
Calculate the capacitance or inductance necessary to achieve resonance in a series RLC circuit.

## Slide 4: Unit 4.7: Resonance in Series RLC Circuits

## Slide 5: Introduction
We learnt in the previous unit that if XL < XC, the RLC circuit will behave inductively and if XC > XL it will behave capacitively.
But what happens when XL = XC? This is the question we will explore in this unit.
XL = XC
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Summary of RL and RC circuits
Before going further, let’s revise some of what we know about series RLC circuits.
XL > XC
XC > XL

## Slide 7: What is resonance?
Let’s do an investigation to work out what happens in a circuit when XL = XC.
Download and work through the worksheet. Then watch the video to make sure you completed everything correctly.
Download the worksheet
Vid01
Notes: Download the worksheet = on click, open Doc01. See appendix for brief
Img01 = EveryCircuit logo
Vid01 = on click, play Vid01 full screen. See appendix for brief

## Slide 8: The resonant frequency
Every series RLC circuit will have a specific frequency at which XL = XC. This is called the resonant frequency of the circuit and is give the symbol fr.
Watch the video to learn more.
Vid02
Notes: Vid02 = on click, play Vid02 full screen. See appendix for brief
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 9: Resonant frequency summary
The following things happen at the resonant frequency:
The inductive reactance (XL) and the capacitive reactance (XC) cancel each other out.
All the opposition to current flow is resistive i.e. Z = R.
1
2
VL = VX are equal but opposite so cancel each other out.
4
The full supply voltage is dropped over the resistor i.e. VT = VR.
5
Click on each point.
Because impedance is a minimum, current is at a maximum.
3
Notes: On click of each number, reveal the whole point.

## Slide 10: Resonance for series RLC circuits?
We need a formula in order to calculate the resonant frequency in any series RLC circuit.
Watch the video to find out what this formula is and how we derive it.
YT01
Notes: YT01 = on click, play YT01 full screen. YT01 = https://www.youtube.com/watch?v=jacrT6mISm0

## Slide 11: Series RLC resonant circuits – example 1
Let’s put all our new knowledge to work with an example.
Redraw the circuit on a blank piece of paper.
The circuit is represented is tuned. Calculate the value of the capacitor.
Note: A tuned circuit is one at resonance.
100V
Notes: Img02 = redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 12: Series RLC resonant circuits – method 1
The first method uses the fact that in a tuned circuit XL = XC.
100V
Calculate the inductive reactance, XL. Enter your answer to three decimal places.
Check
Ω
XL
Notes: Img02
Fill in the blank question
Correct answer: 2764.691Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. XL = 2πfL = 2π x 2x106 x 220x10-6 = 2764.601
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 13: Series RLC resonant circuits – method 1
But we know that XL = XC. So
Rearrange the equation and solve for C, the capacitance of the capacitor. Enter your answer to three decimal places
Check
pF
100V
C
Notes: Img02
Fill in the blank question
Correct answer: 28.784pF
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 14: Series RLC resonant circuits – method 2
Rearrange the equation and solve for C, the capacitance of the capacitor. Enter your answer to three decimal places.
Check
pF
C
100V
The second method uses the resonant frequency formula.
Notes: Img02
Fill in the blank question
Correct answer: 28.784pF
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. L . If you had problems doing this calculation on your calculator, be sure to watch the full worked solution video.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 15: Solving series RLC circuits - solution
Watch the video to see the full worked solution for this question.
You can also have a look at a simulation of the circuit.
Full worked solution
100V
Notes: Img02
Full worked solution = on click, open Vid04 full screen. See appendix for brief.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 16: Tuned circuits can store energy
There is one property of tuned circuits we have not yet touched on. That is their ability to store energy.
Click on the image to open it full screen to learn how this energy is stored.
Img03
Notes: Img03 = on click, open the first frame of the image series full screen. See appendix for brief.

## Slide 17: The basic tuning circuit
One of the many practical uses of resonance is in radio tuning circuits. Here an inductor and variable capacitor are connected in series. When we tune a radio, the LC circuit is set at resonance for a particular radio frequency.
Basic tuning circuits use a variable capacitor to tune into different frequencies.
Watch the video to see how this works in more detail.
Vid04
Notes: Vid04 = on click, play Vid04 full screen. See appendix for brief

## Slide 18: Series RLC resonant circuits – example 2
Calculate the:
Inductive reactance;
Capacitive reactance;
Impedance
Supply current
Voltage across the inductor coil.
Start by drawing and labelling the circuit on a piece of paper.
Here is another resonance circuit example to try.
A 10μF capacitor is connected in series with a 20mH inductor that also has a resistance of 500Ω. The circuit is supplied with 50V at 10kHz.
Represent the resistance of the inductor as a resistor.
Notes: On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 19: Series RLC resonant circuits – step 1
Correct your diagram if you need to.
This is what your circuit diagram should have looked like.
VT = 50V
C =
VC
VL
IL
IC
IT
Notes: Img04 – redraw circuit
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 20: Series RLC resonant circuits – step 2
Now we can start answering the questions.
VT = 50V
C =
VC
VL
IL
IC
IT
Calculate the inductive reactance, XL. Enter your answer to three decimal places.
Check
Ω
XL
Notes: Img04
Fill in the blank question
Correct answer: 1256.637Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. XL = 2πfL = 2π x 10x103 x 20x10-3 = 1256.637Ω
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 21: Series RLC resonant circuits – step 2
VT = 50V
C =
VC
VL
IL
IC
IT
Calculate the capacitive reactance, XC. Enter your answer to three decimal places.
Check
Ω
XC
Notes: Img04
Fill in the blank question
Correct answer: 1.592Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. We know that
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 22: Series RLC resonant circuits – step 2
VT = 50V
C =
VC
VL
IL
IC
IT
Calculate the impedance, Z. Enter your answer to three decimal places.
Check
Ω
XC
Notes: Img04
Fill in the blank question
Correct answer: 1350.977Ω
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 23: Series RLC resonant circuits – step 2
VT = 50V
C =
VC
VL
IL
IC
IT
Calculate the supply current, IT. Enter your answer to three decimal places.
Check
mA
IT
Notes: Img04
Fill in the blank question
Correct answer: 37mA
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct.
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 24: Series RLC resonant circuits – step 2
VT = 50V
C =
VC
VL
IL
IC
IT
Calculate the voltage across the coil, Vcoil. Enter your answer to three decimal places.
Check
V
Vcoil
Notes: Img04
Fill in the blank question
Correct answer: 37mA
Feedback:
Correct – Well done. You got it!
Incorrect – That is not correct. The voltage across the inductor coil needs to take account of the voltage drop due to its inductance and resistance i.e Vcoil = VR + VL. Remember that these are vectors separated by 90 therefore . VR = IT x R = 0.037 x 500 = 18.5V. VL = IT x XL = 0.037 x 1256.637 = 46.496V. Therefore,
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 25: Document Briefing – Doc01 (1 of 3)
Create an annotated PDF worksheet with the following steps.
Make sure you have downloaded the EveryCircuit App from your app store.
If you are working on a computer, visit http://everycircuit.com/app/.
Open the EveryCircuit app and signup. After your trial, you will still have access to EveryCircuit and other people’s circuits. You will just not be able to create your own circuits.
Go to the community space and search for the circuit called “NOC_Resonance”
Open the circuit.
This circuit has an AC power supply with a frequency of 650Hz (or 650 cycles per second) and a peak voltage of 9V. It also has a 30Ω resistor and a 20mH inductor and 2μF capacitor.
Start by making a copy of the following table on a piece of paper.

## Slide 26: Document Briefing – Doc01 (2 of 3)
f | 650Hz | 700Hz | 750Hz | 800Hz | 850Hz | 900Hz | 950Hz
I |  |  |  |  |  |  | 
XL |  |  |  |  |  |  | 
XC |  |  |  |  |  |  | 
Z |  |  |  |  |  |  | 

## Slide 27: Document Briefing – Doc01 (3 of 3)
With the supply frequency at 650Hz, click on the ammeter and write down the value of the circuit current. Also calculate XL, XC and Z.
Now click on the supply and then on the spanner icon. Select Frequency and change it to 700Hz. Write down the values of the circuit current, XL, XC and Z. Note: you may need to give the simulation time to settle on a current value.
Complete the table.
At what frequency is a maximum current reached? What is the total impedance in the circuit when the current is a maximum? What is the relationship between the total impedance and the value of R when the current is a maximum?
What can you say about the values of XL and XC when the current is a maximum?
What are the values for VL and VC when the current is a maximum? Click on the respective voltmeters to find out.
On the same set of axes, draw graphs of XL vs f and XC vs f.
How does this graph relate to the frequency you found at which the current is a maximum?

## Slide 28: Video Briefing – Vid01 (1 of 2)
Create a screencast video presented by an expert presenter. The presenter needs to work through the Doc01 worksheet and cover and explain the following steps.
Opening the app and opening the circuit for mobile and desktop
Complete the table showing how to do at least 1 column’s changes and calculations (see next slide)
Show that max current happens at 800Hz. At this frequency XL = XC but because they are in opposite directions (show a phasor diagram) they cancel each other out.
Explain that the total reactance is thus zero and Z = R. Because impedance is at a minimum, current is at a maximum.
All of this only happens when the frequency is 800Hz.
Show the graphs of XL and XC vs f (see https://www.desmos.com/calculator/cycwnsry8k) and pinpoint where they cross – this frequency is called the resonant frequency (fr )– that frequency where the inductive and capacitive reactances are equal and opposite.

## Slide 29: Video Briefing – Vid01 (2 of 2)
f | 650Hz | 700Hz | 750Hz | 800Hz | 850Hz | 900Hz | 950Hz
I | 175mA | 225mA | 276mA | 299mA | 276mA | 234mA | 195mA
XL | 81.681Ω | 87.965Ω | 94.248Ω | 100.531Ω | 106.814Ω | 113.097Ω | 119.381Ω
XC | 124.291Ω | 115.413Ω | 107.719Ω | 100.987Ω | 95.046Ω | 89.766Ω | 85.041Ω
Z | 52.111Ω | 40.662Ω | 32.886Ω | 30.000Ω | 32.226Ω | 38.004Ω | 45.599Ω

## Slide 30: Video Briefing – Vid02 (1 of 4)
Create a screencast video presented by an expert presenter explaining resonant frequency with the use of the graphics on the next slides:
We know that inductive reactance is proportional to frequency and so the graph of XL vs f looks like this (Img02).
We can also plot capacitive reactance vs frequency. Because XC is inversely proportional to f, the graph looks like this (Img03).
If we combine these graphs we get one that looks like this – it plots reactance vs frequency for both XL and XC (Img04).
There is a point at which these graphs cross – there is a frequency that makes XL = XC.
This specific frequency is called the resonant frequency fr
At frequencies less than fr, we can see that XC > XL and the circuit will behave capacitively.
At frequencies greater than fr, we can see that XL > XC and the circuit will behave inductively.

## Slide 31: Video Briefing – Vid02 (2 of 4)
At fr we know that XL = XC, but because they are equal and opposite they cancel each other out.
Open https://www.desmos.com/calculator/2qtekovc0a
  Here is a simple resonant frequency simulation
  The purple graph is capacitive reactance
  The green graph is inductive reactance
  We can change the values of L and C and we can see that this changes the shape of each graph.
  But there is always a point where they cross. This is fr.
  On the side we have the phasor diagram. As we increase f from zero, we can see that XC is larger than XL and that the circuit is capacitive. The overall voltage lags the current.
  But as we get closer and closer to fr so XC and XL approach the same value until at fr they are equal (but opposite) and cancel each other out. The voltage is in phase with the current and the circuit behaves resistively. In other words there is no reactance and all the impedance is due to resistance i.e. Z = R. At this point Z is at a minimum, therefore I is at a maximum.

## Slide 32: Video Briefing – Vid02 (3 of 4)
  Also at fr, and VL = VC. Remember the voltage drop across these components is in proportion to their reactances so if XL = XC , then VL = VC. But because they are opposite, like reactance, they cancel each other out and all the supply voltage is dropped over the resistor i.e. VT = VR.
  Past fr, XL is bigger than XC and the circuit will be inductive. Overall, voltage will lead current.
  Notice that we can keep frequency the same and change the values of L or C to find resonance.

## Slide 33: Video Briefing – Vid02 (4 of 4)
Notes: Img02 (inductive reactance) = img11 from 01_04_03
Img03 (capacitive reactance) = img17 from 01_04_03
Img04 (combined graphs) = https://www.electronics-tutorials.ws/accircuits/acp204.gif – redraw

## Slide 34: Video Briefing – Vid03 (1 of 3)
Create a screencast video presented by an expert presenter. The presenter needs to work through the question in example 1.
The circuit is represented is tuned. Calculate the value of the capacitor.
Note: A tuned circuit is one at resonance.
100V

## Slide 35: Video Briefing – Vid03 (2 of 3)

## Slide 36: Video Briefing – Vid03 (3 of 3)

## Slide 37: Video Briefing – Vid04 (1 of 1)
Create a screencast video presented by an expert presenter explaining the working of a basic tuning circuit using https://www.desmos.com/calculator/y6pljojunw. Set f = 360, L = 200, C = 1 and R = 200.
Explain the working of a basic tuning circuit.
  If we want to tune into the frequency of 360, we need to increase the capacitance of the capacitor. As we do so, we change the shape of the capacitive reactance graph.
  As we increase C, we eventually tune the circuit by making the XC = XL for the desired frequency. In this simulation, we had to make C = 260.
  The same circuit could, in principle, be designed with a variable inductor but in practice simple tuning circuits use variable capacitors.
  In these circuits, the inductor provides both the inductance and the resistance. Remember that an inductor is really just a piece of wire. It is this wire that offers resistance to the flow of current.

## Slide 38: Image Briefing – Img03 (1 of 5)
Create a set of images with descriptive text as described, including the simple back/forward navigation.
Part A:
In a LC circuit, the capacitor stores energy in the electric field between its plates. The amount of energy depends on the voltage across it. The indictor stores energy in its magnetic field, depending on the current through it.
At some point, the capacitor will be full charged.
Next
Notes: Animation screenshots from https://en.wikipedia.org/wiki/File:Tuned_circuit_animation_3.gif – marked for reuse.

## Slide 39: Image Briefing – Img03 (1 of 5)
Part B:
If an indictor is connected to the capacitor, current will start to flow through the inductor, building up a magnetic field.
Next
Back

## Slide 40: Image Briefing – Img03 (1 of 5)
Part C:
Current will flow until all the charge in the capacitor is gone and its voltage is zero.
Next
Back

## Slide 41: Image Briefing – Img03 (1 of 5)
Part D:
However, the current will continue flowing because an indictor resists changes in current. The current will begin to charge the capacitor with the opposite polarity to before.
Next
Back

## Slide 42: Image Briefing – Img03 (1 of 5)
Part E:
Current will continue to flow until the inductor magnetic field has completely collapsed and all the charge is again stored in the capacitor but with the opposite polarity. The cycle begins again.
Back
Next

## Slide 43: Image Briefing – Img03 (1 of 5)
Part F:
Therefore, charge flows back and forth between the plates of the capacitor through the inductor. Energy would oscillate back and forth between the capacitor and the inductor for ever were it not for the internal resistance in the wires of the circuit.
However, if we connect the circuit to an external AC power supply at the same resonant frequency, we keep the oscillations going.
Back
Notes: This part must have the full repeating animation as found at https://en.wikipedia.org/wiki/File:Tuned_circuit_animation_3.gif