## Slide 1: Electrical components and systems
Topic 1 – Cables and conductors

## Slide 2: Wiring a 16 Ampere plug top
Unit 1.4

## Slide 3: In this lesson you will learn about:
Fitting a 16-ampere plug top to a cable.
Notes: Link each to the relevant section below.

## Slide 4: Inside a 16 Amp plug top
A 16A plug is designed to draw a maximum of 16 Amps from a compatible socket, after which it will start to heat, burn or if it has a fuse it will blow.
Earth
Live
Neutral
Notes: On clicking each conductor in the image present the following:
“EARTH (green or yellow)- The longest pin on the 3 pin plug is attached here. The conductor lengths must be arranged so that if the cable is pulled out of the plug, the earth conductor must only break contact after the live and neutral conductors.”
“LIVE (brown)-The conductor lengths must be arranged so that if the cable is pulled out of the plug, the earth conductor must only break contact after the live and neutral conductors.”
“NEUTRAL (blue)-The conductor lengths must be arranged so that if the cable is pulled out of the plug, the earth conductor must only break contact after the live and neutral conductors.”
Image: https://tinyurl.com/ybwzx3bx

## Slide 5: How to wire a 16 Ampere plug top
Watch the video to learn how to wire a 16 amp plug top. Remember, using damaged tools or wrong tools for the job can cause injury and damage the equipment.
Video 01 Screenshot
Notes: screenshot of vid01 (see brief). Play video full screen.

## Slide 6: Let’s review:
In this lesson we have covered:
Wiring of a 16Amp plug.
Make sure you have a complete understanding of all the work covered here before you start the next unit.

## Slide 7: Quiz time
We have come to the end of this unit. Check your knowledge on how to wire a 16 Amp plug by answering the following questions.

## Slide 8: Question 1
Label the parts of this 3-pin plug.
Earth Pin Green/yellow
Live Pin
Brown
Neutral Pin Blue
Notes: The diagram is currently labelled correctly. Allow students to insert answers next to the pins.

## Slide 9: Question 2
You need to explain the first four steps of wiring a 16 Amp plug to a friend, who missed the practical lesson. Re-arrange the steps below in the correct order.
1) Use a knife to strip the outer insulation off the cable to the length of the plug top. Do not damage the insulation of the three cable leads during this process.
2) Cut the live and neutral conductors to half the length of the plug top. The brown is live, the blue is the neutral and the green/yellow is the earth.
3) Strip about 4 mm of insulation off the end of each conductor.
4) Solder the strip conductor ends with a soldering iron.
Notes: The steps are currently in the correct order and must be mixed up before presenting the question to the student.

## Slide 10: Question 3
The longest pin on the 3 pin plug is the Earth pin.
TRUE
FALSE
Notes: True or False
Correct answer is TRUE
Feedback:
Correct – Well done
Incorrect – That is not correct. The conductor lengths must be arranged so that if the cable is pulled out of the plug, the earth conductor must only break contact after the live and neutral conductors

## Slide 11: Question 4
Have a look at the image below and choose the correct reason why this cable cannot be used.
Conductors are not insulated.
Incorrect colours on insulators.
The live wire has been cut and is no longer safe to use.
The earth wire has been cut and is no longer safe to use.
Notes: MCQ
Correct answer is C.
Feedback:
Correct – Excellent.
Incorrect – Try again. Look closely at the image.
Image: https://tinyurl.com/y9897e8k

## Slide 12: Question 5
Why is it important to learn how to learn how to fit a 16 Amp plug?
It can draw a maximum of 16 Amps from a wall socket.
Most portable equipment gets its supply from a plug socket by means of 3 core flexible cables or flexible cords.
Using the wrong tools for the job can cause injury and damage to equipment.
It is cheaper to do your own home improvements and repairs.
Notes: MCQ
Correct answer is B
Feedback:
Correct – Great job.
Incorrect – Try again.

## Slide 13: How to wire a 16 Ampere plug top - Vid01
Before you start an electrical installation make sure you:
• Always use the correct tool for the job.
• Ensure tools are in good condition.
• Use tools correctly.
• Wear appropriate PPE where necessary.
• Always take good care of tools. Maintain, clean and store it properly.
Using damaged tools or wrong tools for the job can cause injury and damage the equipment.
To avoid injury to any person handling portable electrical equipment it is important that the equipment is kept in a safe condition. Nearly all portable equipment obtain a supply from a plug socket by means of 3 core flexible cables or flexible cords. It is, therefore, essential to fit the 16A plug top correctly.
A plug is a device that :
a) has two or more metallic contacts in the form of pins,
b) is arranged for attachment to a flexible cord or cable, and
c) is intended for engagement with a socket-outlet (SANS 3.5.4)
Notes: Use a Voice over to create a video with script as is here. Create a video similar to this one: https://www.youtube.com/watch?v=cewXz5lzZu8 but in a South African context using a local plug top.

## Slide 14: How to wire a 16 Ampere plug top - Vid01continued
Let’s go over the method to wire or fit a 16 Amp plug top.
Use a knife to strip the outer insulation off the cable to the length of the plug top. Do not damage the insulation of the three cable leads during this process.
Cut the live and neutral conductors to half the length of the plug top. The brown is live, the blue is the neutral and the green/yellow is the earth.
Strip about 4 mm of insulation off the end of each conductor.
Solder the strip conductor ends with a soldering iron. If it is not possible to solder the ends then they must be stripped to about 8 mm, twisted together and doubled over before being placed in the sockets of the pins.
Insert the conductors in their respective positions. Brown – live pin; Blue- neutral pin; Green / Yellow – earth pin.
NOTE: The conductor lengths must be so arranged that if the cable is pulled out of the plug, the earth conductor must only break contact after the live and neutral conductors, i.e. it is the last conductor to break contact with its terminal.
Tighten the screws so that the conductors cannot be pulled out by hand.
Bind cables with cotton-type braided outer insulation as shown in FIG. 5. All inner strings and tapes must be fastened in the cord grips with the cables.
Insert into a non-slip cord grip or fasten it with screw-down clamp, whichever is applicable.
Screw back/replace the cover of the plug top firmly.
Notes: Use a Voice over to create a video with script as is here. Create a video similar to this one: https://www.youtube.com/watch?v=cewXz5lzZu8 but in a South African context using a local plug top.