## Slide 1
Placeholder Diagram needed for an industrial environment ie a factory. Must be similar in style to the example on the right.
Notes: Note for design:
This diagram needs to be redrawn and styled similarly to the example provided.
Note for interactivity:
This should be an interactive map where users are able to click on each of the scenarios on the diagram and be taken to the information for that scenario.

## Slide 2: Wireways
Topic 6 – Motor Controls Centre Scenario
All copyright and intellectual property rights in respect of materials developed by the service provider during this project will vest in the Department of Higher Education and Training, which will have the right to allow any individual, company, agency or organisation to use or modify the materials for any purpose approved by this Department, including selling the materials or releasing them as Open Educational Resources (OER) under an appropriate copyright license.
Notes: Notes for Nick Du Plessis:

## Slide 3: Assumed prior learning
Fundamentals of electricity
Safety, health environment, risk and the quality principles in the workplace
The use of hand and power tools and applicable safety requirements
Measuring and testing methodologies (electrical and mechanical)
Introduction to the world of work and the electrical trade
Don’t feel confident yet about these topics? Click on each to review the content. Feeling confident? Click next to proceed with this unit.
Notes: Interactivity notes:
Each point to take learner to that particular section in course to recap:
Eg.01 = direct learner to Topic X in Course 0

## Slide 4: Disclaimer- Key points about working under supervision
No person may authorize, design, install or permit or require the installation of an electrical installation, other than in accordance with a health and safety standard incorporated into these Regulations under section 44 of the Act. (Electrical installation regulations section 5)
No person may do electrical installation work as an electrical contractor unless that person has been registered as an electrical contractor in terms of these Regulations (Electrical installation regulations section 6)
It must be noted that in terms of Occupational Health & Safety Act all electrical construction work must be conducted under the general control of the registered person, and in terms of this criteria you will not be allowed to work in the distribution board. You will be permitted under the general control of this registered person to do the following work. (Electrical installation regulations section 5)
The registered person will be responsible for issuing the certificate of compliance for this addition to the electrical installation, after he has inspected and tested the electrical installation. (Electrical installation regulations section 9)
During this exercise we will be providing 3 options to provide supply to a gate motor, we are aware that there are many more options and these will be influenced by finance, time, environment and skill.
It must be noted that any other installation must comply to the regulations, standards and manufactures specifications.
I have read and understood all points contained in the Disclaimer.
Notes: Note for navigation on site:
This information needs to stated on the LMS, perhaps as part of the introduction? Applicable to all scenarios for Course: Electrical Installations

## Slide 5: Scenario Outcomes
By the of this unit, you will be able to:
1. Plan a job and understand the regulations applicable to the specific task
2. Select and apply the correct tools for the task
3. Conduct a risk assessment for the task
4. Prepare the worksite
5. Install equipment and materials according to relevant standards, and manufacturer requirements
6. Conduct the required tests for an alteration of an electrical supply
7. Interact with and provide feedback to the client
Notes: Present boxes with just the number. On click/touch, reveal the full statement as a slide right animation
Display small animations to indicate that boxes can be clicked/touched

## Slide 6: Glossary
Add words and terms here….
NOTE for SME:
Please verify and add missing terms.
Notes: Notes for interactivity/development:
There needs to be a searchable glossary with all the electrical terms, techniques, tools equipment. When learner clicks on the word they should be able to see a definition an image/video for each item.
Glossary terms:

## Slide 7: Motor Controls Centre Installation

## Slide 8
Introduction
In this scenario you will learn how to supply power to a motor controls centre.
Important: As the electrician you would install the complete circuit including the socket outlet. The appliance that connects to the Socket Outlet is NOT part of the electrical installation.

## Slide 9
The 8 Steps
In this scenario, you will work through eight key steps.
1
2
4
5
6
7
8
3
Move over each step to find out more. Then, click Next to get started with Step 1.
Notes: Note for development:
There are 8 steps for each of the 6 scenarios in Course 4. Please create suitable graphic to use represent steps and use throughout all scenarios.
Number and relevant graphic to appear at first on each step. Graphics provided here are examples only. Will need to be redrawn.
Learner will click to reveal text description for each box. See below
Mouseover/Popup text
Step 1: Your supervisor gives you a brief
Step 2: You need to identify the best solution for doing the job
Step 3: Plan and design an approach for doing the job
Step 4: Follow the rules and regulations
Step 5: Do a Risk Assessment
Step 6: Complete the job
Step 7: Check if the job was done correctly
Step 8: Do the client handover

## Slide 10: Step 1-Supervisor brief
Imagine that you are an electrician working at a car manufacturing factory. You have just received a call from your supervisor, Mr Dlamini. He needs you to supply power to the motor controls centre.
.
Step 1
Step 2
Step 3
Step 4
Step 5
Step 6
Step 7
Step 8
Click on the clipboard to see the details of this project.
Follow rules and regs
COC required
Follow OHS standards
Don’t damage walls or ceiling boards
Supply from any point installation but must be compliant
Finish in 1 day
CHEAP AS POSSIBLE!
Find out more about 3 phase sockets and how they work.
Notes: Note for interactivity:
When learner clicks on “Find out more” they should be taken to slide 12.
Next button should take them to Slide 13
Text on clipboard should fade in slowly after about 10 seconds.

## Slide 11: What is a motor controls center?
Placeholder for Video 02 on 3 phase sockets:
https://www.youtube.com/watch?v=oyRrm_K7WSM
Link above can be used as reference.
Go back to previous page
Notes: Note for interactivity:
When learner clicks on “Go back to options” button it should take them back to Slide 11

## Slide 12: Supervisor brief
As Mr Dlamini talked you quickly took some notes on a piece of paper. Mr Dlamini will be on leave from tomorrow so you must make sure you have understood everything he said while he is still available to answer your questions.
Get started
Click on the button to get started.
Image of Mr Dlamini talking on the phone standing and looking impatient
Notes: Note for interactivity:
Button “ Go to list for details” should be hyperlinked to questions on Slide 13.

## Slide 13: Client brief
What do you think COC stands for?
Certificate of Commerce
Certificate of Compliance
Commercial Official Certificate
Choose the correct answer from the options below:
Notes: Note for interactivity:
This is a multiple choice question one correct answer.
Correct answer is in italics
Feedback for correct answer. Well done you are correct
Feedback for incorrect answer.
Oops not quite. COC stands for Certificate of Compliance.

## Slide 14: Client brief
What do you think OHS stands for?
Occupational Heath and Safety
Occasional Health and Safety
Official Health and Security
Choose the correct answer from the options below:
Notes: Note for interactivity:
This is a multiple choice question one correct answer.
Correct answer is in italics
Feedback for correct answer. Well done you are correct
Feedback for incorrect answer.
Oops not quite. OHS stands for Occupational Health and Safety

## Slide 15: Client brief
When Mr Dlamini said “ Supply from any point installation but must be compliant” can you explain in your own words what he means?
Type your answer in the block provided and click submit.
Submit
Notes: Note for interactivity:
Text box for typing, when learner clicks submit the should be taken to Slide 16.

## Slide 16: Client brief
When Mr Jansen wrote “ Supply from any point installation but must be compliant” he meant that ……. (get explanation from Nick)
Notes: Note for interactivity:

## Slide 17: Client brief
How many days do you have to complete this job?
1 day
2 days
7 days
As long as I need
Choose the correct answer from the options below:
Notes: Note for interactivity:
This is a multiple choice question one correct answer.
Correct answer is in italics
Feedback for correct answer. Well done you are correct
Feedback for incorrect answer.
Oops not quite. You only have 1 day to finish your work so you will need to work quickly and efficiently.

## Slide 18: Client brief
Why do you think Mr Jansen wrote “CHEAP AS POSSIBLE” in big letters?
Type your answer in the block provided and click submit.
Submit
Notes: Note for interactivity:
Text box for typing, when learner clicks submit the should be taken to Slide 18.

## Slide 19: Area details
It’s very important that you know the details of the area where you will be installing the 3 phase socket. You took a walk around and carefully looked at your surroundings.
Placeholder for Vid03: Area Details
Watch this video for more information about what you found when you walked around the area.
Notes: Note for interactivity:
When learner clicks on video it should appear as full screen.

## Slide 20: Summary of area details
Not sure you can remember all the area details?
(NAME OF factory) area details
Click on the button to download the area details. Keep this list handy for Step 2 coming up next.
Notes: Notes for interactivity:
When user click on the box the following information should appear.
Reviewing the installations the following has been found
There a Sub DB’s surface mounted in the area where the circuit is required
The distance to where the socket outlet is required is 15 meters from the Sub DB and there are 12 slots available in the Sub DB for new circuit breakers and there is an earth leakage in board
There is an existing wire cable basket that runs up the wall and past the point where the socket outlet is required
The supply must be at least 4 mm wire as the current is32 amps for the socket outlet
The protection will need to be a 30A circuit breaker
There is a lot of forklifts and heavy machinery moving around on the premises
There is no ceiling in the plant
There are dogs on the property
There are toilet facilities for staff

## Slide 21: Supervisor brief
Did you listen carefully to what your supervisor said?
See client details
You will be given a list of details from the conversation. Choose all the correct details from this list and click SUBMIT when you are finished.
Notes: Note for interactivity:
Button “ Go to list for details” should be hyperlinked to questions on Slide 13

## Slide 22: Supervisor brief
SUBMIT
Still to add. Need correct client briefing content
Notes: Note for interactivity:
This is a multiple choice question, with multiple answers correct. Correct answers are in italics.
Feedback for ALL correct answers.
Well done! You got them all correct. You are ready to move on to finding out more about your client’s property details. (Go to slide 14)
Feedback for any incorrect answer.
Oops you didn’t get all the correct details. Make sure you listen carefully to what your client has to say. Click here to refresh your mind. (Link to slide 13)(RECAP)

## Slide 23: Supervisor brief
Let’s review the details that Mr Dlamini gave you over the phone.
Click on each of the blocks below to find out more. You will need this information for the remainder of the steps in this scenario.
Notes: Note for interactivity:
Student clicks on each card to flip over/reveal content. Relevant graphics/icon to be created to represent each item which displays before card is flipped. Example provided only- they must be recreated.
Content for blocks:

## Slide 24: Area details
Now that you know what Mr Dlamini, your supervisor wants, you need to find out specific details about the are. You can do this by taking a proper look around. This helps with your planning.
Placeholder for Vid01: Property Details
Watch this video to learn more information about the area.
Notes: Note for interactivity:
When learner clicks on video it should appear as full screen.

## Slide 25: Summary of area details
Can’t remember all the details? Click on the boxes below to refresh your mind.
Tip: Keep the details handy for future reference. Click here to download.
Property Details
Still to add. Need correct client briefing content
Notes: Note for interactivity:
Student clicks on each card to flip over/reveal content. Relevant graphics/icons to be created and displayed on each card to represent each item before it is clicked. Then, when card is clicked, content will display in placeholder box on the right.
Content on cards:
Click Here to be linked to Resource 1 in Appendix. “Client and property details”. Users should be able to download this resource and save it on their computers/phones.

## Slide 26: Step 2- Choose the best option
In this step you first need to weigh up the options and decide which will be the best approach to take. A number of factors could affect your decision.
Environmental conditions
Availability of tools and Equipment
Availability of materials
Time constraints
Availability of labour
Regulation codes and standards
Possible risks
Factors to consider:
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Move over each item to find out what these factors are…
Notes: Note for interactivity:
Picture representing each factor shows initially. Graphic to be recreated. Then, as learner rolls over, description shows.
Descriptions as follows:
Cost restrictions
Environmental conditions
Availability of tools and equipment
Availability of materials
Time constraints
Availability of labour
Regulation codes and standards
Possible risks

## Slide 27: Step 2- Choose the best option
You have three possible options available to you when providing the supply to the motor controls centre.
Option 1
TIP: Keep in mind the information that your client told you and the property details.
Take a look at the options below. You will soon need to decide which option is the best for this job.
Option 2
Option 3
Notes: Note for interactivity:
Each video to play in new window with ability to close and go back to remaining options. See video scripts in appendix
When learner clicks on the “Next” button (standard navigation int the player) they should be taken to next slide- Stop and reflect

## Slide 28: Stop and reflect
Image placeholder to represent option 1
OPTION 1
OPTION 2
So far, which option do you think might be the best for installing the supply for the motor control centre….? Move the slider scale to indicate which option you believe is Good, Better and Best…
Image placeholder to represent option 2
OPTION 2
Image placeholder to represent option 3
OPTION 3
GOOD
BETTER
BEST
GOOD
BETTER
BEST
GOOD
BETTER
BEST
Option 2 and 3 in source content refers to water heater
Notes: Note for interactivity:
1.Create suitable graphics to represent each option at first. When learner mouses over, then details about option display. See below:
2. Create slider scale under each option for learner to select good, better and best option.
Option 1: ( to be displayed when flashcard moused over)
Use 4mm Armoured (2+E) cable to supply a 3 phase motor controls centre
Option 2:
Option 3:

## Slide 29: Stop and reflect
You chose Option X as the best option for the job. Why? Type a reason in the text area below and click submit.
Submit
Notes: Note for interactivity:
The bold text “Option X’ in the instruction box needs to be replaced with whatever option the learner chose as the BEST option in the previous slide.
Text box, learner should be able to type in a response. There is no correct answer, this question is to be the learner thinking.
When learner clicks on the Submit button they should be taken to Slide 20

## Slide 30: Factors to consider
We know that there are a number of factors will affect the option you finally choose to complete the job.
Option 1
Option 2
Option 3
What to Consider?
Review each option to see what you need to consider.
Cost
Environmental conditions
Tools & Equipment
Materials
Time
Labour
Codes and Standards
Possible risks
Notes: Note for interactivity:
When learner clicks on each of the options blocks they should be taken to the following slides:
Option 1- Slide 21
Option 2- Slide 22
Option 3- Slide 23
When all options have been completed, the NEXT button will only appear
When learner rolls over each icon, the following description will display (ALL graphics need to be redrawn)
Money

## Slide 31: Option 1: Details
Tools and equipment
Use 4mm Armoured (2+E) cable to supply a 3 phase motor controls centre
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk implications
Click on each of the boxes to find out more.
Go Back
Notes: Note for interactivity:
When learner clicks on each of the boxes, information for that box should be revealed. Create icon/graphic to show on each card with the text before it is flipped over. See details below:
Tools and equipment
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk Implications

## Slide 32: Option 2: Details
Click on each of the boxes to find out more.
Tools and equipment
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk implications
Go Back
Still to add. Need correct options
Notes: Note for interactivity:
When learner clicks on each of the boxes, information for that box should be revealed. See details below:
Tools and equipment
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk Implications

## Slide 33: Option 3: Details
Click on each of the boxes to find out more.
Tools and equipment
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk implications
Go Back
Still to add. Need correct options
Notes: Note for interactivity:
When learner clicks on each of the boxes, information for that box should be revealed. See details below:
Tools and equipment
Materials
Time
Labour
Cost
Environmental implications
Regulations
Risk Implications

## Slide 34: Advantages and Disadvantages
OPTION 1
Advantages
Image placeholder to represent option 1
OPTION 2
Image placeholder to represent option 2
OPTION 3
Image placeholder to represent option 3
Disadvantages
Before you choose the best option for this job, you should weigh up the advantages and disadvantages. Click on each option to view.
Still to add. Need correct options
Notes: Note for interactivity:
When learner mouses over each graphic, the description for that option appears.
When learner CLICKS on each of the boxes, information for that box should be revealed on the boxes on the right. See details below:
Option 1 Description mouse over text: Use 4mm Armoured (2+E) cable to supply a 3 phase motor controls center
Option 2 Description mouse over text:
Option 3 Description mouse over text:
When learner CLICKS on an option, the advantages and disadvantages display in boxes on rhs:
Option 1:
Advantages
This appears to be the cheapest and most cost effective method to get the supply from the DB 1 to the new water heater supply
Disadvantages
Norsk cable is more expensive than flat twin ands earth
Option 2:
Advantages
Flat twin and earth is cheapest cable to install and a very effective method to get the supply from the DB 1 to the new water heater supply
With this cable you have no mechanical protection
It is flexible to work with
Disadvantages
Option 3:
Advantages
Fairly cheap method
Disadvantages
Does not meet client requirement that installation must be compliant to manufactures requirements and standards

## Slide 35: Choose the best option
Submit
Option 1
Time to select the best option for this job. Choose an answer and click submit. You may review the options before deciding.
Option 2
Option 3
Still to add. Need correct options
Notes: Note for interactivity:
Three options imbedded. Learner can click to view in new window. Video scripts in appendix – see option 1, 2 and 3 video scripts.
Multiple choice, feedback below: (correct answer in italics)
Option 1 Feedback:
Option 2 Feedback:
Option 3 Feedback:

## Slide 36
As Option X is the most cost effective option, we will use it for the rest of the scenario. But how do you even begin to think about all the things you will need to do the job..?
Step 3- Plan the job
1
2
3
4
5
6
7
8
Placeholder video:
How to plan for the job, must include info about working through the steps in your head and thinking about what you will need for each step to make sure you don’t miss anything. Must discuss tools, equipment, materials, PPE. Its an overview.
Watch this video for advice from an experienced electrician on how to properly plan for a job.

## Slide 37
Step 3- Plan the job
Draw your plan
Select tools and equipment
Select materials
Select PPE
1
2
3
4
5
6
7
8
Let’s review what needs to be done as part of proper job planning.
Notes: Graphics to represent each block to be recreated.
Link each block to corresponding slide that follows
Draw plan- slide 28
Identify tools – slide 32
Identify materials- slide 35
Select PPE – slide 37
As learner reviews all elements, they need to come back here. Only when all has been viewed, can they proceed to next section- Step 4

## Slide 38: Draw your plan
The plan is used by you and your team when you go to a client’s property.
Placeholder-Video 05
Take a look at this video which explains how the plan is created.
Notes: Note for interactivity:
When user clicks on the video it should appear as full screen. Link to video in appendix

## Slide 39: Draw your plan
You are going to now draw your OWN plan for Option X.
Use the property details, job instructions and video for Option X to draw your own plan. You can use paper or a computer programme to make your drawing.
Area details
Step by step instructions
Video of Option 1
I need help with drawing my plan
Notes: Note for interactivity:
When learner clicks on “Property” block they should see Resource 01
When learner clicks on Video – they should see Option 1 Video in Appendix
When learner clicks on “I need help” they should be taken to the relevant topic in Course 0: World of Electrician
When learner clicks on “Step by step” block they should see the following information:
STEPS:
Measure, mark and mount a flush mount enclosure in a roof onto a rafter within arms reach of the water heater
Connect GP conductors to isolator
Drill a hole using a holesaw in enclosure for a gland
Connect an appliance using Norsk cable into an enclosure
Using cable clips Saddling multicore cable onto wood or rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars NOTE : always leave some slack in the wire minimum 200mm
Switch off supply to DB1 and test to ensure safe to work
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect supply from earth leakage supply to circuit breaker to new water heater supply in BD
Conduct relevant tests
Complete COC
Hand over to client
When learner clicks on “Video” block they should see Video Option 1

## Slide 40: Upload your plan
Submit
Submit your plan so that it can be saved in your ePortfolio. Upload your plan and click submit.
Notes: Note for interactivity:
The word ePortfolio should be linked to information about what an ePortfolio is and how it works, how learner can access it.
There needs to be an upload function for user to upload their plan.

## Slide 41: The completed plan
How does your completed plan look? Your plan should resemble something like this.
Still to add. Need correct plan diagram
Notes: Note for interactivity:
Recreate plan

## Slide 42: Identify tools and equipment
Submit
Screwdriver (terminal, flat, star)
Side cutter
Hammer
Pliers
Fish tape
Wire strippers
Ladder
Placeholder for another tool
Placeholder for another tool
Placeholder for another tool
Placeholder for another tool
Which tools do you think are needed to complete this job? Click on each tool to find out more about its purpose. Then, drag and drop your chosen tools into the tool box.
Placeholder for another tool
Still to add. Need correct options
Notes: Note for interactivity:
Create images to use for each item instead of the text box
This is a drag and drop activity. Learner should be able to drag and drop the each tool to the image of the toolbox.
When they click on the submit button they should be taken to feedback page. – see below
When the learner clicks on each tool, the corresponding info should appear. See example on Slide 34 of suggest layout for each tool.
Correct tools:
Hammer
Screwdriver ( terminal, Flat, star)
Side cutter
Wire strippers
Pliers
Fish tape
Ladder
Incorrect tools - OTHER OPTIONS TO INCLUDE
Drill
Hacksaw
Bender spring
Multi meter
Scriber
Feedback for correct answer:
Well done! You have chosen the correct tools for this job. (learner should proceed)
Feedback for incorrect answer:
Oops not quite. You are missing some essential tools for this job. Not to worry on the next page we will review the tools needed for this job. (learner should be taken to Slide 33)

## Slide 43: Tools for the job
Hammer
Image of a hammer
Short description of what a hammer does.
Not too sure which tools were required? Don’t worry, we have listed them here again. Mouse over each one to review their intended use.
Notes: NOTE TO MEDIA DESIGN TEAM:
Show all picture icons for each of the CORRECT tools. Student can rollover each one to review the details for each. Details to display in block. Refreshes to display new info pertaining to each tool selected.

## Slide 44: Placeholder for tool descriptions
Hammer
Image of a hammer
Short description of what a hammer does.

## Slide 45: Materials
12 meters of 2,5mm flat twin and earth
Label (water heater/geyser)
1 x Isolator enclosure complete
2,5mm saddles
20A Circuit breaker 3KA
In order to complete this job you will need materials such as wires and connectors. Click on each box below to see more information.
Still to add. Need correct options
Notes: Note for interactivity:
When user clicks on each of the blocks, another block with information about each material should appear. See Slide 36 for example.

## Slide 46: Placeholder for material descriptions
Circuit breaker
Image of PVC cable
Short description of a circuit breaker and what it is used for.

## Slide 47: Personal protective equipment (PPE)
When completing a job you must always make sure that you are protecting yourself and the people who are working with you. One of the ways you do that is by making sure you and your team are wearing the correcting personal protective equipment or PPE.
Placeholder-Video 06 - PPE
Watch this video on PPE to find out why its so important.
Notes: Note for interactivity:
When learner clicks on video it should play full screen. Refer to Appendix for video

## Slide 48: Select the correct PPE
Placeholder:
Image of an electrician (he should not be wearing any PPE)
Submit
Choose the PPE you think you would need for this job. Drag and drop the items onto the image of the electrician. Click ‘submit’ once you are done.
Tip: Not sure what each item is used for? Click on each to view a description first.
Still to add. Need correct options
Notes: Note for interactivity:
Drag and drop activity. Electrician does not have any safety equipment/gear on to start. As student drops into correct place, then it displays on him. Need to include some completely incorrect choices up front as well. Icons used here are examples only. Need to create relevant icons in accordance with correct options specified below.
User can click on each item to view more info before dragging and dropping – See slide 39 as example
Correct items to be dropped onto the image are:
Overall
Safety shoes
Safety glasses
When learner clicks on ‘submit’ button they should be taken to feedback page.
Feedback if correct: Well done! You have chosen the correct PPE for completing this job.
Feedback if incorrect: Oops not quite, the correct PPE needed for this job was :
Overall
Safety shoes
Safety glasses

## Slide 49: Placeholder for PPE descriptions
Safety glasses
Image of safety glasses
Short description of safety glasses and what it is used for.

## Slide 50
Another name for rules and regulations is codes. As an electrician you need to follow the SANS (South African National Standards) codes. These can be tricky to understand at first.
Step 4 - Follow rules and regulations
Placeholder: Video o7 and Vid 08 combined into 1
1
2
3
4
5
6
7
8
Watch the video to find out how to read and apply a SANS code correctly.
Notes: Note for interactivity:
When learner clicks on videos they should appear as full screen.

## Slide 51: Multiple choice
Add question based on Vid 07 and 08 scripts (Dave Gravett)
Examples of questions:
What is the best way to read the code?
When reading the code you should focus on which part?
What parts are not important?
Do codes get updated? Then what?
Choose the correct answer from the options below.

## Slide 52: SANS Codes
There is one SANS code that you need to be aware of when installing the supply for a water heater.
Click on the code to find out what it covers. You will be asked questions about it in the next activity.
SANS 10142-1
Notes: Note for content development:
See if there is a step by step process that comes out of Video 07 and 08 and then use that structure here. Ie. Step 1 Scan for information, Step 2 highlight the important part.
Note for interactivity:
When learner clicks on each of the SANS codes they should be taken to the following slides:
SANS 10142-1: Slide 43

## Slide 53: SANS 10142-1
Scrollable text.
Read through the document below and then click on the ‘Next’ button to answer some questions about this code.
Notes: NB: Licensing issue. I see that there is a copyright on the SANS codes. Do we need to apply for permission from SABS to use them in our learning materials?
Note for interactivity:
SANS document text should be inserted on this page in a scrollable window so that learner can read the entire document on this screen.

## Slide 54: Multiple choice
Insert questions from Dave Gravette here
Verify that the voltage drop are within the permitted range
Verify that the method of installation is expectable
of cable installation is applied.
OHS ACT

## Slide 55: Step 5- Do a risk assessment
A risk assessment involves taking a careful look at your workplace to identify those things, situations and processes that could put you or your team in danger. You should always do a risk assessment before you begin any job.
Placeholder: Video 9 and Video 10 combined into one video on Risk assessment
1
2
3
4
5
6
7
8
Can’t remember what a risk assessment is? Watch the video to refresh your mind.
Notes: Reference back to Course 0 but still ask them to do a specific risk assessment activity.

## Slide 56: Step 5- Identify the risks
Time to have some fun and identify some potential risks. From the list below, match the task with a potential risk when installing the supply to the motor controls centre.
Add tasks and risks
Notes: Notes for interactivity:
Matching activity. The order should be shuffled. Here are the correct pairs:
Feedback if answer is correct- Well done! You matched the correct risks with the correct tasks. (Take learner to slide 67)
Feedback if answer is incorrect- Oops not quite. On the following page you will see the tasks and the risks that go with those tasks. (66)

## Slide 57: Step 6- Complete the job
Well done on getting this far! To complete the job for, you need to now carry out the tasks required.
Task 1
Task 2
Task 3
Task 4
Task 5
Task 6
Task 7
task 8
Task 9
Task 10
Task 11
1
2
3
4
5
6
7
8
Watch the videos to see how each task is performed.
Still to add. Need correct options
Notes: Each block links to the relevant video of task – See appendix for example of layout for each video
Measure, mark and mount a flush mount enclosure in a roof onto a rafter within arms reach of the water heater
Connect GP conductors to isolator
Drill a hole using a holesaw in enclosure for a gland
Connect an appliance using norsk cable into an enclosure
Using cable clips Saddling multicore cable onto wood or rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars NOTE : always leave some slack in the wire minimum 200mm
Switch off supply to DB1 and test to ensure safe to work
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect supply from earth leakage supply to circuit breaker to new water heater supply in BD
Conduct relevant tests

## Slide 58: Step 6- Complete the job
Submit
Measure, mark and mount a flush mount enclosure in a roof onto a rafter within arms reach of the water heater
Connect an appliance using norsk cable into an enclosure
Drill a hole using a holesaw in enclosure for a gland
Switch off supply to DB1 and test to ensure safe to work
Conduct relevant tests
Saddling multicore cable onto wood or rafters to DB1
Oh No! These steps for installing the supply for the motor controls centre are not in the correct order! Drag and drop them into the correct sequence. Click submit when you are done.
Still to add. Need correct options
Notes: Note for interactivity;
Recreate boxes for each element so that all 11 steps are shown, have only created a few here as an example.
Users must be able to move the videos into the correct order. Correct order supplied below:
Measure, mark and mount a flush mount enclosure in a roof onto a rafter within arms reach of the water heater
Connect GP conductors to isolator
Drill a hole using a holesaw in enclosure for a gland
Connect an appliance using norsk cable into an enclosure
Using cable clips Saddling multicore cable onto wood or rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars NOTE : always leave some slack in the wire minimum 200mm
Switch off supply to DB1 and test to ensure safe to work
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect supply from earth leakage supply to circuit breaker to new water heater supply in BD
Conduct relevant tests
Feedback:
Feedback if correct: Well done! You have placed all the steps for completing this job in the correct order..
Feedback if incorrect: Oops not quite, the correct order of steps is:
(Show correct order as per above)

## Slide 59: Step 7- Check job done correctly
Once you have completed the job you must check that everything was done correctly.
Placeholder image representing relevant text
Placeholder image representing relevant text
Placeholder image representing relevant text
Placeholder image representing relevant text
Placeholder image representing relevant text
Placeholder image representing relevant text
1
2
3
4
5
6
7
8
Click on each block below to see what you should check for this job.
Notes: Note for design:
There needs to be an image to accompany each one of these blocks. When student clicks on block, it flips over to reveal text below:
The cable is level and parallel and secured properly
The isolator is square, level and parallel and secured properly
Correct lengths of conductor left in socket outlet and DB
Connections tight at termination points
Circuit labeled water heater on DB 1

## Slide 60: Step 7- Check job done correctly
In addition to checking the elements, you must make sure that the No Voltage Tests and Voltage On Tests are completed.
No Voltage Tests
Placeholder: Insulation resistance test
Continuity of the earth conductor
Voltage On Tests
Simulation:
Polarity Test
Simulation:
Voltage Test
Simulation
Elevated Voltage to Neutral test
Need Dave/Nick’s help in building out the values that would be needed here
Still to add. Need correct options
Notes: Note for interactivity:
When learner clicks on simulation it should appear full screen.
(These tests belong in Course 2)
Focus on range of acceptable values what does it indicate when values are out of this range.

## Slide 61: Step 8- Handover to client
You are almost finished installing the supply for the motor controls centre. The final step is to show your supervisor what you have done.
Placeholder for Video on Handover
How long is a certificate of compliance valid for?
1
2
3
4
5
6
7
8
Watch the videos to find out about COC’s and to see how a client handover is done.
Placeholder for Video on Handover
Notes: Note for interactivity:
Video- see appendix. Video should play full screen when clicked. See appendix – Client handover
Video- see appendix. Video should play full screen when clicked. See appendix – COC Video

## Slide 62: Conclusion
Congratulations! You have now worked through the entire scenario for installing a motor controls centre supply.
There are 5 more scenarios for you to try, would you like to try one now?
Scenario: Gate Motor Supply
Scenario: Security Light
Scenario: Water Heater Supply
Scenario: 3 Phase socket outlet installation
Scenario: Motor controls centre installation
Notes: Note for interactivity:
Interactive map allowing learners to go to remaining scenarios. Student should click on each one to be able to go directly there.
“

## Slide 63
ICONS REQUIRED
ICON REQUIRED | ICON PURPOSE | Example:
Outcomes | Icon to represent Learning Outcomes | 
Extra Information | Icon to represent Additional Information | 
Instruction | Icon/ Or actual person to represent an Instruction (something learner needs to do) | 
Tip | Icon to represent a hint or tip | 
Glossary | Icon to represent Glossary Page | 
Reflection | Icon to represent Reflection | 
Important point |  | 
Notes: Icons to be re-created and used across all UNITS. These are examples only.

## Slide 64: Animated scenario: 01: Client brief
Voice of an middle-aged white male, speaking over a phone with the electrician:
Client: Hello, this is Ted Pretorius. Are you John of Expert Electricians?
Electrician: Yes. How can I help you?
Client: I need you to provide a supply for my water heater and its rather urgent.
Electrician: I see. When do you need the job done by?
Client: I am expecting visitors over the week-end, so need you to complete the job in two days. The sooner you can start, the better!
Electrician: That should not be a problem. My team and I can have the work done by the end of the week. What else can you tell me? Do you have any constraints?
Client: Great to hear! The insurance is not going to cover this work, so I need you conduct the work in the cheapest way possible, while still adhering to all the required regulations and standards.
Electrician: Of course! We are committed to adhering to all regulations as well as health and safety standards. Do you have any requests about how we need to do the work? Or where my team and I can get the supply?
Client: Please make sure that activities do not damage the walls or look unsightly. You are also not allowed to chase the walls or damage ceiling boards. You can get the supply from any point in the installation as long as it is compliant.
Electrician: No problem. Will you be available tomorrow so my team and I can do a property visit?
Client: Yes, that would be great. One more thing, I will need you to provide a certificate of compliance when the job is done.
Electrician: Of course! See you tomorrow Mr Pretorius!
Notes: Note for interactivity:
Rebuild this as an animated scenario embedded into content. Create characters/personas for the two individuals.. It is a phone call between the two characters. Audio and visual should play for relevant person. Characters to be in different poses and positions.

## Slide 65: Vid 01: Property details
Animated video using a tool like GoAnimate. Black and white hand drawn images with a voice over. Each point should be on a separate slide.
Script for voice over:
When you visited Mr Pretorius’s property, here is what you found:
There are 2 DB’s . One in the main house (BD 1), which is flush mounted and one in the garage (BD 2), which is surface mounted.
The heater that has been installed by the plumber is 8 meters from DB1. There are 2 slots available in the DB for new circuit breakers and there is an earth leakage in board
The heater is 16 meters from the DB2. There are 9 slots available in the DB for new circuit breakers and there is an earth leakage in board
The roof is pitched and easy to move around
There are spare pipes in the wall to feed the supply from the DB’s into the roof space
The water heater is 2kw and is used for the kitchen
The supply must be at least 2,5mm wire as the current is 9,66 amps for the water heater
The protection will need to be a 20A circuit breaker
There is no ceiling in the garage
There are dogs on the property
There are toilet facilities for staff

## Slide 66: Vid 02: Step 2 Option 1
Demonstration video with voice over and text banners appearing as action on the video is completed.
Use 2,5mm Norsk (2+E) cable to supply a isolator that will allow the water heater to be supplied from
Measure, mark and mount a flush mount enclosure in a roof onto a rafter within arms reach of the water heater
Connect GP conductors to isolator
Drill a hole using a holesaw in enclosure for a gland
Connect an appliance using norsk cable into an enclosure
Using cable clips Saddling multicore cable onto wood or rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars NOTE : always leave some slack in the wire minimum 200mm
Switch off supply to DB1 and test to ensure safe to work
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect supply from earth leakage supply to circuit breaker to new water heater supply in BD
Conduct relevant tests
Complete COC
Hand over to client

## Slide 67: Vid 03: Step 2 Option 2
Demonstration video with voice over and text banners appearing as action on the video is completed.
Use 2,5mm flat twin and earth (2+E) cable to supply a isolator that will allow the water heater to be supplied from
Mount the isolator enclosure onto a rafter within arms reach of the water heater
Switch off supply to DB1 and test to ensure safe to work
Connect conductors to isolator
Drill 20mm hole in enclosure for the gland
Fit a PVC gland onto enclosure
Using cable clips saddle flat twin and earth cable to rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars NOTE : always leave some slack in the wire minimum 200mm
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect new water heater supply conductors in BD
Conduct relevant tests
Complete COC
Hand over to client

## Slide 68: Vid 04: Step 2 Option 3
Demonstration video with voice over and text banners appearing as action on the video is completed.
Use 2,5mm Norsk (2+E) cable to supply a isolator that will allow the water heater to be supplied from
Switch off supply to DB1 and test to ensure safe to work
Connect conductors to water heater
Using cable clips saddle norsk cable to rafters to DB1
We will draw in the cable into the spare conduit into the DB1
Strip sheath off cable allowing sufficient length for cores to reach the new circuit breaker as well as earth and neutral bars. NOTE : always leave some slack in the wire minimum 200mm
Fit 20 Amp circuit breaker in DB and connect supply from earth leakage supply to circuit breaker
Connect new water heater supply conductors in BD
Conduct relevant tests
Complete COC
Hand over to client
NOTE there must be an isolator on a water heater installation within arms reach regulation

## Slide 69: Vid 05: How to draw a plan
Demonstration video with electrician talking to the learner about how to do the plan, interspersed with screenshots of him doing the plan.
This link can be used as a basis: https://www.bhg.com/home-improvement/electrical/how-to-draw-electrical-plans/
Notes: Video script for placeholder on Slide 3.

## Slide 70: Vid 6: Personal protective equipment
An animated video discussing the following:
What is PPE
Why do we wear it?
What are the most common PPE for electricians?
Where can you find/buy PPE? (Is it your responsibility or that of your employer?
Notes: Video script for placeholder on Slide 3.

## Slide 71: Vid 07: Overview of the SANS codes and how they work
Animated video using a tool like GoAnimate. Black and white hand drawn images with a voice over.
SANS, refers to a standard that specifies the performance requirements of a specific product. A SANS standard may be either locally written or created by adopting an international (usually ISO) standard.
What does a SANS code look like?
Why do we have them?
Where can we access them?
What happens when the code changes? Does this happen often?

## Slide 72: Vid 08: Overview of the SANS codes and how they work
Demonstration video. Take an example of a SANS code (ie SANS 10142). Video should alternate between showing the facilitator talking and screenshots of the SANS code as demonstrator highlights various aspects of it.
Information that should be covered in this video:
How do we read a SANS code? (Highlight important info in the document for learner)
How to we apply the SANS code?
Notes: Video script for placeholder on Slide 3.

## Slide 73: Vid 9:Risk Assessment
An animated video discussing the following:
A risk assessment is a term used to describe the overall process or method where you:
Identify hazards and risk factors that have the potential to cause harm (hazard identification).
Analyse and evaluate the risk associated with that hazard (risk analysis, and risk evaluation).
Determine appropriate ways to eliminate the hazard, or control the risk when the hazard cannot be eliminated (risk control).
A risk assessment is a thorough look at your workplace to identify those things, situations, processes, etc. that may cause harm, particularly to people. After identification is made, you analyse and evaluate how likely and severe the risk is. When this determination is made, you can next, decide what measures should be in place to effectively eliminate or control the harm from happening.

## Slide 74: Vid 10: 5 Steps of doing a Risk Assessment
An animated video discussing the following:
ACTIVITY
HAZARD
DANGER
RISK (without preventative measures)
PREVENTIVE MEASURE
Must mention the difference between a hazard and a danger.

## Slide 75: Video example for each task : Complete the task
Demonstration Video showing:
Drill a hole in a wall (Module 19)

## Slide 76: Video : Client Handover
Demonstration Video showing the electrician interacting with the client:
Conduct walk about with client showing:
the route of the wire way of installation
Indicate the positioning of the breaker and where it is installed.
Provide the client with the certificate of compliance (COC) as per legislation explaining its purpose as well clients responsibility in terms of maintain the electrical installation

## Slide 77: Video : COC
Discussion with qualified electrician discussing the following:
What is a COC?
Who can issue a COC?
What does a COC look like?
How long is a COC valid for?

## Slide 78: Resource 01: Client brief and property details
Client Brief:
The project must follow all regulations and standards
You need to provide the client with a certificate of compliance
Health and safety regulations must be complied to at all times
You can get the supply from any point in the installation as long as it is compliant
Activities must NOT damage the walls or look unsightly
You are NOT allowed to chase the walls and damage ceiling boards
You must finish all the work in 2 days
Financial resources are very limited and you need to do the work as cheap as possible
Property details:
There are 2 DB’s . One in the main house (BD 1), which is flush mounted and one in the garage (BD 2), which is surface mounted.
The heater that has been installed by the plumber is 8 meters from DB1. There are 2 slots available in the DB for new circuit breakers and there is an earth leakage in board
The heater is 16 meters from the DB2. There are 9 slots available in the DB for new circuit breakers and there is an earth leakage in board
The roof is pitched and easy to move around
There are spare pipes in the wall to feed the supply from the DB’s into the roof space
The water heater is 2kw and is used for the kitchen
The supply must be at least 2,5mm wire as the current is 9,66 amps for the water heater
The protection will need to be a 20A circuit breaker
There is no ceiling in the garage
There are dogs on the property
There are toilet facilities for staff
Placeholder for visual representation/diagram of property details
Notes: Notes:
Recreate and format downloadable sheet into visually appealing format with suitable imagery and graphics
If possible, create schematic diagram which shows layout of property