## Slide 1: Single Phase Motors
Topic 2: The Different Types and Uses of Single Phase Motors

## Slide 2: Assumed prior learning
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
Text
Notes: Note for design:
This list of text should be broken up to make it more interesting. Text should be presented in a menu type of format.
Note for interactivity:
Information should be presented in a clickable menu so that learner can click on each outcome instead of it being one long list.

## Slide 4: Unit 2.2: Non-Capacitor Motors

## Slide 5: Introduction
In the previous unit, we saw that many single phase motors use capacitors to increase the phase angle between the starting and running windings
But capacitors are big, expensive and can break. Centrifugal switches can also break. So there are a few single phase motors that use other ways to simulate a rotating magnetic field.
To mimic a rotating magnetic field
1
Increase torque
2

## Slide 6: Single Phase Non- Capacitor Induction Motors
There are three basic kinds of single phase motors that DO NOT use a capacitor to create a rotating magnetic field.
Shaded Pole
Universal
Synchronous
Quiz
Click on each button to find out more.
You must remember that all three types are still induction motors and work because the stator magnetic field induces a current in the rotor which creates a rotor magnetic field.
Notes: Button 1 = Goto Slide 7
Button 2 = Goto Slide
Button 3 = Goto Slide
Suppress navigation
As user returns to this menu, indicate which motors they have viewed. When all motors have been viewed, display the Quick Quiz button instead.
Button 04 = Goto slide 20

## Slide 7: Shade Pole Motors
They do not have the normal stator windings.
Their rotors are very similar to other induction motor rotors.
Watch the video to learn more about shaded pole motors.
Vid01
Shaded pole motors are ingenious.
Notes: Play Vid01 (see brief) full screen.

## Slide 8: Uses of Shaded Pole Motors
Shaded pole motors are common but the stator field is weak. They have very low torque.
They are relatively inefficient.
There are no moving parts so they are cheap and reliable.
Img02
Img03
Img04
Conveyor Belt
Desk fan
Compressor
Click on the image below that uses a shade pole motor.
Back to
motor menu
Notes: Img02 = conveyor belt
Img03 = desk fan
Img04 = compressor
Correct image is Img03. Provide feedback on selection of each:
Img02 – A conveyor belt often has heavy things on it when it starts up. Therefore you need a string motor with good starting torque. The shaded pole motor has weak starting torque.
Img03 – Yes, a desk fan is a perfect application. Low starting torque is needed and the motor does not need to be very powerful.
Img04 – Compressors often have to work under different loads so you need a powerful motor with good running torque that can hand different loads. Shaded pole motors do not have great running torque.
For all three images, add view full screen option.
Button 1 = Goto Slide 6

## Slide 9: Synchronous Motors
Synchronous motors are a variant of shaded pole motors and are very similar in construction, except for the rotor.
Img05
Unlike most induction motors, they are synchronous – they spin at the same rate as the stator rotating magnetic field.
Notes: Img05 = image of synchronous motor – e.g. https://5.imimg.com/data5/WA/UB/MY-1979015/single-phase-ac-synchronous-motor-250x250.jpg

## Slide 10: The Secret is in the Rotor
The secret of the synchronous motor is in the rotor and what it’s made of. The rotor is a set of disks made out of a magnetic material like cobolt. But why?
Cobalt is used because it can be easily magnetised.
Vid02
Watch the video to find out.
Notes: Play vid02 (see brief) full screen

## Slide 11
Synchronous motors spin at eth same rate as the rotating magnetic field in the stator
Notes: Play vid02 (see brief) full screen

## Slide 12: Uses of Synchronous Motors
As a kind of shaded pole motor, synchronous motors tend to be small and low powered (between 10 – 25 watts). But they are great at maintaining constant speed even under different loads.
Click each box to see some typical uses.
1
2
3
Notes: Img06 = picture of CD or DVD player with strap “CD and DVD players”
Img07 = picture of a wall clock with strap “clocks and other timing devices”
Img08 = picture of a turn table with strap “turn tables and record players”
Magnification option available after initial box click and image reveal

## Slide 13: Disadvantages of Synchronous Motors
For all the benefits of running at a constant speed under differing loads, synchronous motors do have some disadvantages.
They are less efficient than other motors.
1
They have quite low torque.
2
They are only available as small motors
3
Back to
motor menu
Notes: Button 1 = Goto Slide 6

## Slide 14: Universal Motors
These motors work with both single phase AC and DC electricity hence the name Universal.
Img09
They can do this because the rotor is connected in series with the stator via a commutator, just like a DC motor.
Therefore, universal motors do not rely on any current being induced in the rotor to cause rotation.
Notes: Img09 = picture of a universal motor showing the rotor commutator.

## Slide 15
The key difference between universal motors and all the other single phase motors is that universal motors are NOT INDUCTION MOTORS.
Notes: Button 1 = Goto Slide 6

## Slide 16: How Do They Work?
Watch this video about how universal motors work.
Take careful note of the 2 important differences between universal motors and ordinary DC motors.
Notes: YouTube URL - https://www.youtube.com/watch?v=0PDRJKz-mqE. Play video full screen.

## Slide 17: What Are They Good For?
Universal motors are used in a wide variety of small and hand held tools and appliances. They have good starting torque but run dangerously fast without a load. Therefore, they are usually direct drive and connected via a set of gears.
Click each box to see some typical uses.
1
2
3
Back to
motor menu
Notes: Img10 = picture of hand drill with the strap “power tools like hand drills”
Img11 = picture of a vacuum cleaner with strap “household appliances like vacuum cleaners”
Img12 = picture of a food processor with strap “appliances like blenders and food processors”
Magnification option available after initial box click and image reveal
Button 1 = Goto Slide 6

## Slide 18: A Quick Quiz
Before we end off, take some time to check your understanding of what we have covered in this unit by answering the following questions.

## Slide 19: Question 1
Which of the following would a synchronous motor be a good choice of motor for?
A hand drill
A sewing machine
An electronic clock
A conveyor belt
Notes: Multiple choice
Correct answer is c). Feedback

## Slide 20: Question 2
Why are shade pole motors low power motors?
They are small
They have a rotor made out of cobolt
They have few moving parts
There are significant power losses in the stator due to the copper rings
Notes: Multiple choice
Correct answer is d). Feedback

## Slide 21: Question 3
Which of the following statements about synchronous motors are true?
They are induction motors.
They rotate slower than the stator rotating magnetic field.
They are used in many household appliances.
They are small, low powered motors.
Notes: Multiple correct
Correct answers are a) and d). Feedback:

## Slide 22: Question 4
What are the differences between universal motors and DC motors. Choose all that apply.
Universal motors have a commutator.
Universal motors have high resistance brushes.
Universal motors have a stator made of laminations.
Universal motors can run on DC power.
Notes: Multiple correct
Correct answers are b) and c)
Feedback:
Both DC and universal motors have a commutator.
Only – This is a difference between universal and DC motors but there is another one – the stator is made up of laminations.
Only - This is a difference between universal and DC motors but there is another one – the brushes are high resistance brushes.
b) And c) – Well done. Those are the 2 key differences.
d) Both DC and universal motors can run on DC power.

## Slide 23: Video Briefing – Vid01
Voiced animation or whiteboard video demonstrating how shaded pole motors work.
Show the structure of the motor including
  Stator winding
  Iron core
  Copper rings
  Rotor – highlight that it is basically the same as other induction motors
Explain how flux is set up in iron core based on induced magnetic field of stator windings
Explain how the flux changes through the core and what happens at the copper poles
  As flux increases we have changing magnetic field
  Induces current in copper rings
  Current produces magnetic field in opposition to the one that created it (Lenz’s Law) so flux does not get past copper rings
  As flux stays the same, no induced current and flux present past copper rings
  As flux decreases, we have another changing magnetic field
  Induces current in copper rings
  Current produces magnetic field in opposition so flux concentrated past rings
  End result is a rotating magnetic field
Talk about key characteristics
  Small, low power – 5W to 40W – power low due to losses in the stator due to copper rings
  Low starting torque
  Low running torque
  Cheap and reliable
Notes: See https://www.youtube.com/watch?v=MyEnwJ1Lazg as a reference

## Slide 24: Video Briefing – Vid02
Voiced animation and demonstration video demonstrating how single phase synchronous motors work.
Show construction of motor including:
  Shaded pole stator
  Rotor with cobolt (or similar material) and rotor bars
Explain how motor works
  When the stator is energised with single-phase AC, the rotating stator field induces a current in the rotor cross bars and the motor starts as an induction motor. At the same time as the motor develops speed, the disk rotor becomes magnetised (hysteresis)
  Hysteresis occurs when a magnetic material is placed in a magnetic field and the electrons of the material align itself with the field flux and the material itself becomes magnetised. If the field is rotated, the electrons of the rotor must also turn to maintain alignment with that of the field.
  During the acceleration period, the stator field will be rotating faster than the rotor. When the rotor speed reaches the synchronous speed of the field, the rotor poles will take up fixed positions, and at this point will lock into synchronism with the rotating stator field.