## Slide 1: Three Phase Motors
Topic 1: How Three Phase Motors Work

## Slide 2: Assumed prior learning
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of the unit you will be able to:
Notes: Note for design:
This list of text should be broken up to make it more interesting. Text should be presented in a menu type of format.
Note for interactivity:
Information should be presented in a clickable menu so that learner can click on each outcome instead of it being one long list.

## Slide 4: Unit 1.4: Synchronous Speed and Slip

## Slide 5: Introduction
Remember this question we asked in unit 2 of this topic?
It is the rotating magnetic field of the stator cutting the rotor bars that induces a current in the rotor bars.
1
It is this induced current that creates a magnetic field on the rotor that then tries to follow the stator.
2
Remember
What would happen if the rotor of an induction motor were to spin at the same rate as the rotating magnetic field of the stator?
Notes: Present boxes with just the number. On click/touch, reveal the full statement as a slide right animation
Display small animations to indicate that boxes can be clicked/touched

## Slide 6: Why the rotor is always slower
If the rotor spins at the same rate as the stator rotating magnetic field then there is…
No relative motion between the rotating field and rotor
1
No inducted current means the rotor is no longer an electromagnet.
3
No relative motion means no induced current in the rotor bars.
2
This means that there will be no force to spin the rotor and the rotor will slow down again restoring relative motion.
4
Click the numbers to read more.
Notes: Only display numbers – only allow numbers to be click in success. On click of a number reveal the point.

## Slide 7: Synchronous speed
We call the speed at which the stator magnetic field rotates synchronous speed. We calculate the synchronous speed of a motor with this equation.
This equation gives us revolutions per minute (rpm).
Img01
Notes: Img01 (see brief)

## Slide 8: A quick note on poles
Most induction motors have 4 or 6 poles but some motors have 2 or 8 poles. But what exactly is a pole.
Img01a
Click on the image to learn more.
Notes: Img01a = see brief
On each successive click, scroll through all the images in the Img01a brief.

## Slide 9: How does the equation work?
Take a look at this motor. We can see that it has 2 poles per phase. What happens, if we supply the motor with 50Hz AC power? How many times, per minute will the stator magnetic field spin round?
Img01b
Watch the video to see if you are right
Notes: Img01b = Img01a part 1
Watch the video to see if you are right = on click, play Vid01 full screen (see brief)

## Slide 10: Example 1
What is the synchronous speed of a 4 pole motor connected to 50Hz three phase power?
50 rpm
1,500 rpm
9.6 rpm
1,500 rps
Notes: MCQ
Correct answer is b
Feedback:
a) – That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula . In this case f = 50Hz and p = 4. Therefore, rpm.
b) – Well done. That is correct. rpm
c) – That is not correct. It looks like you have have swopped the value of f and p. f is frequency which in this case was 50Hz. P is the number of motor poles which in this case was 4. . Therefore, rpm.
d) – That is not correct. While the number is right, the units should be rpm (revolutions per minute) not rps (revolutions per second). You would have to divide 1,500 by 60 to calculate the revolutions per second.
MCQ
Correct answer is b
Feedback:
a) – That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula 𝑁_𝑠=120𝑓/𝑝. In this case f = 50Hz and p = 4. Therefore, 𝑁_𝑠=(120×50)/4=1,500 rpm.
b) – Well done. That is correct. 𝑁_𝑠=(120×50)/4=1,500 rpm
c) – That is not correct. It looks like you have have swopped the value of f and p. f is frequency which in this case was 50Hz. P is the number of motor poles which in this case was 4. 𝑁_𝑠=120𝑓/𝑝. Therefore, 𝑁_𝑠=(120×50)/4=1,500 rpm.
d) – That is not correct. While the number is right, the units should be rpm (revolutions per minute) not rps (revolutions per second). You would have to divide 1,500 by 60 to calculate the revolutions per second.

## Slide 11: Example 2
What is the synchronous speed of a 6 pole motor connected to 60Hz three phase power?
60 rpm
12 rpm
1,200 rpm
1,300 rpm
Notes: MCQ
Correct answer is c
Feedback:
– That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula . In this case f = 50Hz and p = 4. Therefore, rpm.
– That is not correct. It looks like you have have swopped the value of f and p. f is frequency which in this case was 60Hz. P is the number of motor poles which in this case was 6. . Therefore, rpm.
c) – Well done. That is correct. rpm.
d) – That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula. In this case f = 50Hz and p = 4. Therefore, rpm.
MCQ
Correct answer is c
Feedback:
– That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula 𝑁_𝑠=120𝑓/𝑝. In this case f = 50Hz and p = 4. Therefore, 𝑁_𝑠=(120×60)/6=1,200 rpm.
– That is not correct. It looks like you have have swopped the value of f and p. f is frequency which in this case was 60Hz. P is the number of motor poles which in this case was 6. 𝑁_𝑠=120𝑓/𝑝. Therefore, 𝑁_𝑠=(120×60)/6=1,200 rpm.
c) – Well done. That is correct. 𝑁_𝑠=(120×60)/6=1,200 rpm.
d) – That is not correct. To calculate the synchronous speed of this motor, we need to use the synchronous speed formula 𝑁_𝑠=120𝑓/𝑝. In this case f = 50Hz and p = 4. Therefore, 𝑁_𝑠=(120×60)/6=1,200 rpm.

## Slide 12: Example 3
A motor is known to have a synchronous speed of 750rpm when connected to 50Hz power. How many poles does it have.
2
4
6
8
Notes: MCQ
Correct answer is d
Feedback:
– That is not correct. In this case we know what Ns is. We have to rearrange the equation to solve for p. Therefore, . Ns = 750rpm and f = 50Hz. So The motor has 8 poles.
– That is not correct. In this case we know what Ns is. We have to rearrange the equation to solve for p. Therefore, . Ns = 750rpm and f = 50Hz. So The motor has 8 poles.
That is not correct. In this case we know what Ns is. We have to rearrange the equation to solve for p. Therefore, . Ns = 750rpm and f = 50Hz. So The motor has 8 poles.
d) – Well done. We had to calculate p this time so we needed to rearrange the equation to solve for p. The motor has 8 poles.
MCQ
Correct answer is d
Feedback:
– That is not correct. In this case we know what Ns is. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for p. Therefore, p=120𝑓/𝑁_𝑠 . Ns = 750rpm and f = 50Hz. So p=(120×50)/750=8. The motor has 8 poles.
– That is not correct. In this case we know what Ns is. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for p. Therefore, p=120𝑓/𝑁_𝑠 . Ns = 750rpm and f = 50Hz. So p=(120×50)/750=8. The motor has 8 poles.
That is not correct. In this case we know what Ns is. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for p. Therefore, p=120𝑓/𝑁_𝑠 . Ns = 750rpm and f = 50Hz. So p=(120×50)/750=8. The motor has 8 poles.
d) – Well done. We had to calculate p this time so we needed to rearrange the equation to solve for p. p=(120×50)/750=8. The motor has 8 poles.

## Slide 13: Example 4
A 2 pole motor is known to have a synchronous speed of 3600rpm. What power source must it be supplied to have this synchronous speed?
50Hz
55Hz
60Hz
65Hz
Notes: MCQ
Correct answer is c
Feedback:
– That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the equation to solve for f. Therefore, . So The motor must be supplied with 60Hz power.
– That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the equation to solve for f. Therefore, . So The motor must be supplied with 60Hz power.
Well done. You got it. We have to rearrange the equation to solve for f. Therefore,
That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the equation to solve for f. Therefore, . So The motor must be supplied with 60Hz power.
MCQ
Correct answer is c
Feedback:
– That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for f. Therefore, f=(𝑁_𝑠 𝑝)/120. So f=(3600×2)/120=60Hz The motor must be supplied with 60Hz power.
– That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for f. Therefore, f=(𝑁_𝑠 𝑝)/120. So f=(3600×2)/120=60Hz The motor must be supplied with 60Hz power.
Well done. You got it. We have to rearrange the equation to solve for f. Therefore, f=(𝑁_𝑠 𝑝)/120=(3600×2)/120=60𝐻𝑧.
That is not correct. In this case we know what Ns and p are but need to find f. We have to rearrange the〖 𝑁〗_𝑠=120𝑓/𝑝 equation to solve for f. Therefore, f=(𝑁_𝑠 𝑝)/120. So f=(3600×2)/120=60Hz The motor must be supplied with 60Hz power.

## Slide 14: Example 5
True or false: A 4 pole induction motor will have a higher synchronous speed the higher the frequency of the power supplied to it.
True
False
Notes: MCQ
Correct answer is a
Feedback:
– Well done. That is correct. In the equation the greater f is the greater Ns will be.
- That is not correct. In the equation the greater f is the greater Ns will be.
MCQ
Correct answer is a
Feedback:
– Well done. That is correct. In the equation 〖 𝑁〗_𝑠=120𝑓/𝑝 the greater f is the greater Ns will be.
- That is not correct. In the equation 〖 𝑁〗_𝑠=120𝑓/𝑝 the greater f is the greater Ns will be.

## Slide 15: Example 6
If we wanted a 6 pole motor to run at a synchronous speed of 2,800rpm, what frequency would the power supplied to it need to be?
Submit
Hz
Notes: Fill in the blank
Correct answer is 140Hz
Feedback:
Correct – Well done. Hz.
Incorrect – Oops. That is not correct. We need to find f so we must first rearrange our equation as follows: . Now, we know that the motor has 6 poles (p = 6) and we want to obtain a synchronous speed of 2,800rpm (Ns = 2,800rpm). Therefore, Hz.
Fill in the blank
Correct answer is 140Hz
Feedback:
Correct – Well done. f=(2800×6)/120=140Hz.
Incorrect – Oops. That is not correct. We need to find f so we must first rearrange our equation as follows: f=(𝑁_𝑠 𝑝)/120. Now, we know that the motor has 6 poles (p = 6) and we want to obtain a synchronous speed of 2,800rpm (Ns = 2,800rpm). Therefore, f=(2800×6)/120=140Hz.

## Slide 16: Slip
We know, however, that induction motors cannot run at synchronous speed. They must always spin more slowly.
The difference between synchronous speed NS and rotor speed NR is called slip and it is always expressed as a percentage of the synchronous speed.
Img02
Notes: Img02 = see brief

## Slide 17
To calculate a motor’s slip, we need its synchronous speed and its rotor speed. This information can be found on the motor nameplate.
Notes: Button 1 = link to full screen popup of vid02 (see brief)

## Slide 18: Example 1
The nameplate speed of a 50Hz, 4-pole induction motor is 1440 RPM. Calculate the percentage slip.
3%
4%
5%
6%
Notes: MCQ
Correct answer is b
Feedback:
a) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
b) - Well done. You got it. The first thing we need to do is calculate the synchronous speed of the motor. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
c) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
d) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
MCQ
Correct answer is b
Feedback:
a) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. 𝑁_𝑆=(120×50)/4=1500 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1500−1440)/1500×100=4%.
b) - Well done. You got it. The first thing we need to do is calculate the synchronous speed of the motor. 𝑁_𝑆=(120×50)/4=1500 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1500−1440)/1500×100=4%.
c) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. 𝑁_𝑆=(120×50)/4=1500 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1500−1440)/1500×100=4%.
d) – That is not correct. The first thing we need to do is calculate the synchronous speed of the motor. 𝑁_𝑆=(120×50)/4=1500 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1500−1440)/1500×100=4%.

## Slide 19: Example 2
What is the slip of this 4 pole motor?
0.8%
1%
2%
4%
Notes: Img03 = https://qph.fs.quoracdn.net/main-qimg-1611a1bbf416cf2b12ba99c1d420490c
MCQ
Correct answer is a
Feedback:
a) – Well done. You got it. We can see that the rotor speed is given as 1785. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
b) - That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
c) – That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
d) – That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
Img03 = https://qph.fs.quoracdn.net/main-qimg-1611a1bbf416cf2b12ba99c1d420490c
MCQ
Correct answer is a
Feedback:
a) – Well done. You got it. We can see that the rotor speed is given as 1785. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. 𝑁_𝑆=(120×60)/4=1800 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1800−1785)/1800×100=0.8%.
b) - That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. 𝑁_𝑆=(120×60)/4=1800 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1800−1785)/1800×100=0.8%.
c) – That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. 𝑁_𝑆=(120×60)/4=1800 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1800−1785)/1800×100=0.8%.
d) – That is not correct. The rotor speed is given as 1785 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 60Hz. 𝑁_𝑆=(120×60)/4=1800 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (1800−1785)/1800×100=0.8%.

## Slide 20: Example 2
What is the slip of this 2 pole motor?
7%
8%
9%
10%
Notes: Img04 = https://upload.wikimedia.org/wikipedia/commons/f/f9/Motor_nameplate_Malmbergs.jpg
MCQ
Correct answer is c
Feedback:
a) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
b) - That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
c) – Well done. The synchronous speed of this motor is 3000rpm. We calculate the slip as .
d) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
Img04 = https://upload.wikimedia.org/wikipedia/commons/f/f9/Motor_nameplate_Malmbergs.jpg
MCQ
Correct answer is c
Feedback:
a) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
b) - That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
c) – Well done. The synchronous speed of this motor is 3000rpm. We calculate the slip as 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
d) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.

## Slide 21: Example 3
A 4 pole 50Hz motor has a known slip of about 5.5%. What is its rotor speed?
7%
8%
9%
1490rpm
Notes: Img04 = https://upload.wikimedia.org/wikipedia/commons/f/f9/Motor_nameplate_Malmbergs.jpg
MCQ
Correct answer is c
Feedback:
a) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
b) - That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
c) – Well done. The synchronous speed of this motor is 3000rpm. We calculate the slip as .
d) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. .
Img04 = https://upload.wikimedia.org/wikipedia/commons/f/f9/Motor_nameplate_Malmbergs.jpg
MCQ
Correct answer is c
Feedback:
a) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
b) - That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
c) – Well done. The synchronous speed of this motor is 3000rpm. We calculate the slip as 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.
d) – That is not correct. The rotor speed is given as 2730 rpm. The first thing we need to do is calculate the synchronous speed of the motor. We can see that the frequency is 50Hz. 𝑁_𝑆=(120×50)/2=3000 rpm. Now that we have the synchronous speed and the rotor speed, we can calculate the slip. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100= (3000−2730)/3000×100=9%.

## Slide 22: Example 4
If this motor has a slip of about 6%, how many poles does it have?
4
3
2
8
Notes: Img05 = https://file2.engineering.com/july-2014/motor-plate.jpg
MCQ
Correct answer is a
Feedback:
a) – Brilliant. You got it. You first calculated the synchronous speed as about 1,840.4rpm and with that found that with a slip of about 6%, the motor has 4 poles.
b), c), d) - That is not correct. We know that the skip is about 6% and we also know the rotor speed is 1730rpm. Therefore we can work out the synchronous speed. We also know that this motor is designed to run on 60Hz so with NS and f we can calculate p. Here is how. . Therefore . If we put the numbers in that we know, we get that . Now, if we multiply both sides by NS we get . If we get all the terms with NS in them to one side we get . Now we have to take out NS as a common factor on the left hand side. . Now we can divide both sides by 0.06 - 1 and solve for NS. . So we know that the synchronous speed is about 1,840.4rpm. We use this to finally solve for p. 3.9. Therefore, is this motor has a slip of about 6%, it has 4 poles.
Img05 = https://file2.engineering.com/july-2014/motor-plate.jpg
MCQ
Correct answer is a
Feedback:
a) – Brilliant. You got it. You first calculated the synchronous speed as about 1,840.4rpm and with that found that with a slip of about 6%, the motor has 4 poles.
b), c), d) - That is not correct. We know that the skip is about 6% and we also know the rotor speed is 1730rpm. Therefore we can work out the synchronous speed. We also know that this motor is designed to run on 60Hz so with NS and f we can calculate p. Here is how. 𝑆=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 ×100. Therefore 𝑆/100=(𝑁_𝑆−𝑁_𝑅)/𝑁_𝑆 . If we put the numbers in that we know, we get that 6/100=0.06=(𝑁_𝑆−1730)/𝑁_𝑆 . Now, if we multiply both sides by NS we get 0.06×𝑁_𝑆=𝑁_𝑆−1730. If we get all the terms with NS in them to one side we get 0.06×𝑁_𝑆−𝑁_𝑆=−1730. Now we have to take out NS as a common factor on the left hand side. 𝑁_𝑆 (0.06−1)=−1730. Now we can divide both sides by 0.06 - 1 and solve for NS. 𝑁_𝑆=(−1730)/(0.06−1)=1840.4. So we know that the synchronous speed is about 1,840.4rpm. We use this to finally solve for p. 𝑝=120𝑓/𝑁_𝑆 =(120×60)/1840.4=3.9. Therefore, is this motor has a slip of about 6%, it has 4 poles.

## Slide 23: Image Briefing – Img01
Ns is the symbol we use for synchronous speed
p is the number of poles per phase the motor has
f is the frequency of the three phase power. In SA this is always 50Hz.

## Slide 24: Image Briefing – Img01a (1 of 3)
For each of the three phases there are 2 poles (or 1 pair of poles) that when energised produce an alternating N and S pole. This is a 2 pole motor. There are 6 poles altogether but only 2 poles per phase.
2-pole, 3-phase motor

## Slide 25: Image Briefing – Img01a (2 of 3)
For each of the three phases there are 4 poles (2 pairs of coils) that when energised produce an alternating N and S pole. This is a 4 pole motor. Each pair of coils is connected so that they are energised at the same time.
4-pole, 3-phase motor

## Slide 26: Image Briefing – Img01a (3 of 3)
For each of the three phases there are 6 poles (3 pairs of coils) that when energised produce an alternating N and S pole. This is a 6 pole motor. The more poles a motor has the smoother it runs.
6-pole, 3-phase motor

## Slide 27: Video Briefing – Vid01 (1 of 2)
Produce a screencast video with an expert electrician explaining how the synchronous speed equation works. Use images like those on next slide to aid the explanation.
If the AC supply is at 50Hz, it means that each phase repeats 50 times per second.
In a 2 pole, three phase motor, looking at phase 1 (yellow), if the initial orientation is NS (top to bottom), half way through the cycle it will be SN (a 180° rotation)and at the end of the cycle it will be back to NS (a full 360° rotation). This repeats 50 times per second which means that the stator magnetic field will rotate 50 times per second.
If it rotates 50 times per second, it will rotate 50x60 = 3000 times per minute. This is the Synchronous Speed given as Revolutions Per Minute.
Look now at the 4 pole, three phase motor. If the initial orientation of the yellow phase is NS (top to bottom) then half way through the cycle it will have rotated 90°. After one full cycle it will have rotated 180°. It will take 2 full cycles to rotate a full 360°. Therefore, it will only make 25 full rotations per second or 25x60 = 1500 rotations per minute. The synchronous speed will thus be 1500rpm.
To make the second calculation look like the first one, we can change it to 50x60/2 or supply frequency times 60 all divided by 2. To make the first equation look like this, we can write it as 50x60/1
So we now have an equation that is supply frequency x 60 / number of pole pairs per phase. But motors are named according to the total number of poles they have per phase – in our case 2 poles and 4 poles.
If we multiply the denominator in each equation by 2, we must also multiply the numerator. This is where the 120 comes from.
In our cases the synchronous speeds are given by supply frequency x 120 / number of poles per phase or 50 x 120/2 and 50 x 120/4.

## Slide 28: Video Briefing – Vid01
2-pole, 3-phase motor
4-pole, 3-phase motor

## Slide 29: Image Briefing – Img02
S
Ns is still the symbol we use for synchronous speed
Multiplying by 100 gives us an answer as a percentage
NR is the symbol we use for rotor speed
S is the symbol we use for slip