## Slide 1: Three Phase Motors
Topic 2: Testing Three Phase Motors

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
By the end of this unit the learner will be able to:
List the necessary single phase motor mechanical tests
Perform the necessary single phase motor mechanical tests
Complete a motor test form with mechanical test results

## Slide 4: Unit 2.1: Three Phase Motor Mechanical Tests and Servicing

## Slide 5: Introduction
Three phase induction motors, especially squirrel cage motors, are tough…really tough!
This is one of the reasons why they are so widely used and can be used in some pretty harsh environments like mines and factories.
Notes: Img01 = image of an induction motor in a real industrial setting e.g. https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcRUTKiDbgTaEgPU_xrZEqvsrHMZHHKtUoYzJbieDykYp3EiWepH

## Slide 6: Why test?
Faulty motors are unsafe and some faults can lead to injury or death.
Maintenance helps keep the motor running correctly and efficiently
There are moving and electrical parts which can wear out.
Motors are often moved and reinstalled which means lifting, handling and transporting.
But nothing is perfect so all three phase induction motors need to be regularly maintained and tested. Here’s why.
1
2
3
4

## Slide 7: Safety first
When you work with motors you must put your safety and the safety of others first. You must complete the necessary Hazard Identification and Control (HIAC) Form.
Get help with HIAC Forms
Need help with HIACs? Click the button to go to Topic X in The World of an Electrician
Notes: Img02 = https://cdn.pixabay.com/photo/2014/04/02/10/38/sign-304093_960_720.png
Button 01 = direct learner to Topic X in Course 0

## Slide 8: Potential Hazards
Here are some of the potential hazards you should look out for:
Vehicles, traffic or mobile equipment
Hazardous Materials or Waste
Electricity, machinery, stored energy or machine isolation
Working at heights above 2m
Lifting and material handling
Work with Oxy-fuel gas mixtures
Notes: Present boxes with just a representative icon in each circle. On click/touch, reveal the full statement.
Display small animations to indicate that boxes can be clicked/touched

## Slide 9: Stop and Check?
Because there are some potential hazards associated with this job, you need to check that all the necessary safety controls related to these hazards are in place.
Learn about Safety Controls
If you are not sure what these safety controls are, you should stop this unit and refer back to Topic X in The World of an Electrician before continuing.
Notes: Img03 = https://upload.wikimedia.org/wikipedia/commons/9/9d/Stop_sign_light_red.svg
Button 01 = direct learner to Topic X in Course 0

## Slide 10: Before We Begin
Before you do any electrical tests, you must make sure that you have isolated and locked out the supply to the motor.
Learn about Isolating and Lock-Out Procedures
Make sure you know how to do this by referring to Topic X in The World of An Electrician.
Notes: Img04 = https://cdn.pixabay.com/photo/2016/07/01/22/38/industrial-safety-1492062_960_720.png
Button 01 = direct learner to Topic X in Course 0

## Slide 11: Things to Test
There are a couple of things to check on a three phase motor. Here is a simple mnemonic to help you remember the list.
Big
Sliced
Sharp
File
Thread
Nylon
Click on each word to find out what to test.
Why not try making your own mnemonic to help you remember what mechanical tests to perform.
Notes: On click/touch of each work present the following in a full screen popup window with clear close button
Bearings – see slide 12
Shaft (and keyways) – see slide 13
Fan (and fan cover) – see slide 14
Stator frame – see slide 15
Name plate – see slide 16
Terminal box – see slide 17

## Slide 12: Bearing Test
To test the bearings you need to rotate the shaft by hand and listen for any clicking or grinding noises. These noises may indicate worn bearings.
You also need to check for any sideways and back and forth movement of the shaft. Any such movement can also indicate worn bearings.
Vid01
Notes: Vid01 – play video full screen

## Slide 13: Shaft and Keyway
Check to see if the shaft is bent in any way. Use a dial gauge indicator to ensure that there is no deflection over 0,02mm.
Also check that the keyway is not damaged in any way.
Vid02
Notes: Vid02 – play video full screen

## Slide 14: Fan and Fan Cover
Check that no motor fan blades are missing and that none of them have any cracks or are broken in any way. Also check that the fan shaft is not loose in any way.
If the motor has an external fan, make sure that the fan cover is firmly in place will all screws present and tight.
Vid03
Notes: Vid03 – play video full screen

## Slide 15: Stator Frame and End Shields
You need to check that the stator frame and end plates have no cracks or other damage. Make sure that there are no broken parts or missing bolts or screws.
If there is a grease housing, check that it is not leaking and has no cracks or other visible damage.
Vid04
Notes: Vid03 – play video full screen

## Slide 16: Name Plate
Check that the name plate is present and that all the information on it is clearly readable.
Img04
Notes: Img04 – image of 2 nameplates – left hand side is damaged and some parts are not readable; right hand side is not damaged and is readable; let hand side has a cross through it.

## Slide 17: Terminal Box
Look for any damage to the terminal box like cracks. Also make sure that all the terminal box screws are present and tight.
Open the terminal box and make sure that the terminal block and all the terminal studs are undamaged.
Img05
Notes: Img05 – image of a terminal box in good order

## Slide 18: Complete A Motor Test Form
You must record all your mechanical tests and findings on a motor test form.
Watch the video of mechanical tests being performed on a motor. Make notes of the test results on a piece of paper as you watch them.
Vid05
Notes: Play vid05 (see brief) full screen.

## Slide 19: Fill in the Results
Complete this online mechanical motor test form with the results of the tests you saw in the video.
Mechanical Test | Pass / Fail | If Fail, reason
Bearings |  | 
Shaft |  | 
Keyway |  | 
Stator Frame |  | 
NDE Shield |  | 
DE Shield |  | 
Fan |  | 
Fan Cover |  | 
Terminal Box |  | 
Terminal Block and Studs |  | 
Name Plate |  | 
Submit
See the tests again
Notes: Place form table in a scrollable box
Pass / Fail column
Pass / Fail option dropdown in each row
If Fail column
Textbox in each row
Button 01 = on submit check entered result of each test and display feedback. Feedback only available once vid05 is produced and it is clear what tests pass and fail.
Button 02 = link to vid05. Play video full screen

## Slide 20: Motor Servicing
Besides simply performing mechanical tests, you must also be able to fully service three phase induction motors.
Watch the video on motor services to get an overview of what this entails.
Vid06
Notes: Play vid05 (see brief) full screen.

## Slide 21: Video Briefing – Vid01
Video of an electrician demonstrating how to test the bearings. Demonstrate on a sound and unsound motor. In particular demonstrate the following:
Sound of worn bearings
Excessive shaft movement
Notes: See https://www.dropbox.com/s/c81f26n10t91c89/Testing%20Electrical%20motors.m4v?dl=0 as a reference

## Slide 22: Video Briefing – Vid02
Video of an electrician demonstrating how to test the shaft. Demonstrate how to use and read a guage indicator. Show readings from a straight and bent shaft.
Notes: See https://www.dropbox.com/s/c81f26n10t91c89/Testing%20Electrical%20motors.m4v?dl=0 as a reference

## Slide 23: Video Briefing – Vid03
Video of an electrician demonstrating how to check the fan. Demonstrate what signs of damage and cracks to look out for.
Notes: See https://www.dropbox.com/s/c81f26n10t91c89/Testing%20Electrical%20motors.m4v?dl=0 as a reference

## Slide 24: Video Briefing – Vid04
Video of an electrician demonstrating how to check the stator frame and end plates. Demonstrate what signs of damage and cracks to look out for and how to check a grease housing and what problems to look out for.
Notes: See https://www.dropbox.com/s/c81f26n10t91c89/Testing%20Electrical%20motors.m4v?dl=0 as a reference

## Slide 25: Video Briefing – Vid05
Video of an electrician conducting all the mechanical tests. Electrician notes what test if being performed but does not say anything about what the test reveals. Some tests pass and some tests fail. It is dependent on the test motor that is available as to what tests pass and fail.

## Slide 26: Video Briefing – Vid06
Video of an electrician conducting a full motor service including
Dismantling
  Remove fan cowling
  Remove fan
  Motor frame cleaning
  Mark and remove end shields
  Clean shaft and remove bearings and retainer plates
Inspection
  Shorted windings and blackening
  Check rotor
  Bearings
  End shields and bearing supports
  Fasteners
  Fan and fan cover
Bearing replacement and assembly
  Bearing heating to 90 degree C
  Replaced on shaft
  Replace rotor with wrapped bearings
  Bearing packed with clean grease (type on nameplate)
  Replace endshileds
  Secure everything
  Replace fan and cover
  Bench run
Notes: See https://www.dropbox.com/s/4l8tn4dbekjtqgp/Three%20phase%20motor%20service.m4v?dl=0 as a reference