## Slide 1: Electronics
Topic 5: Inductors

## Slide 2: Assumed prior learning
05_01_00
05_01_02
05_02_01
05_03_01
05_04_01
Notes: Note for navigation on site:
This information needs to be taken into account and needs to stated on the LMS, perhaps as part of the introduction?

## Slide 3: Outcomes
.
By the end of this unit the learner will be able to:
Explain how inductors in series and parallel work
Calculate total inductance in a circuit

## Slide 4: Unit 5.2: Inductor Characteristics

## Slide 5: Introduction?
In the last unit we saw that inductors oppose changes in current. In AC circuits, where current is always changing, they offer high resistance in the form of inductive reactance.
In this unit we are going to take a look at how inductors behave in series and parallel.
Notes: Img01 = https://upload.wikimedia.org/wikipedia/commons/9/9e/Common_mode_choke_2A_with_20mH_inductance.jpg
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 6: Inductors in series
Let’s take some time to see how inductors behave in series in AC circuits.
Download and work through the worksheet. Then watch the video to make sure you completed everything correctly.
Download the worksheet
Vid01
Notes: Download the worksheet = open Doc01 (see appendix)
Img02 = EveryCircuit logo
Vid01 = On click, play video full screen. See appendix for brief

## Slide 7: Inductors in Series
It turns out that inductors in series work the same way as resistors in series.
Img03
Img04
Capacitors in SERIES
Resistors in SERIES
Notes: Img03 = L1 + L2 + L3 + … = LT
Img04 = R1 + R2 + R3 + … = RT
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 8: Inductors in parallel
You can probably already guess how inductors in parallel behave. But let’s take a look to be sure.
Download and work through the worksheet. Then watch the video to make sure you completed everything correctly.
Download the worksheet
Vid02
Notes: Download the worksheet = open Doc02 (see appendix)
Img02 = EveryCircuit logo
Vid02 = On click, play video full screen. See appendix for brief

## Slide 9: Inductors in Parallel
It turns out that inductors in parallel work the same way as resistors in parallel.
Img05
Img06
Inductors in PARALLEL
Resistors in PARALLEL
Notes: Img05 =
Img06 =
On click of each button present a pop-up with the indicated text:
1 – Resistors in series: When resistors are in series in a circuit, we add up their values to find the total resistance. Note that this applies to any components in a ciruit that supply resistance.
2 – Resistors in parallel: When resistors are in parallel in a circuit, we use the following formula to work out the total resistance
1/𝑅_𝑇 =1/𝑅1+1/𝑅2+…+1/𝑅𝑛
Note that this applies to any components in a ciruit that supply resistance.
3 – Kirchoff’s Voltage Law: Resistors in series divide up the voltage in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.
4 – Kirchoff’s Current Law: Resistors in parallel divide up the current in proportion to their resistances. Note that this applies to any components in a ciruit that supply resistance.

## Slide 10: Test Yourself
We have come to the end of this unit. Answer the following questions to make sure you understand how inductors behave in series and parallel circuits..

## Slide 11: Question 1
True or False: When inductors are connected in parallel, the total inductance is more than a single inductor.
True
False
Notes: Multiple choice question
Correct answer is b
Feedback:

## Slide 12: Question 2
True or False: When inductors are connected in series, the total inductance is more than a single inductor.
True
False
Notes: Multiple choice question
Correct answer is a
Feedback:

## Slide 13: Question 3
Calculate the total inductance in a circuit with a 6mH and a 4mH inductor connected in series.
Notes: Fill in the blank question
Correct answer is 10mH
Feedback:

## Slide 14: Question 4
Calculate the total inductance of a circuit where an 8H, 6H and 3H inductor are connected in parallel.
Notes: Fill in the blank question
Correct answer is 1.6H
Feedback:

## Slide 15: Question 5
Calculate the total inductance in a circuit with 4 identical 4.5mH inductors connected in parallel to 2 decimal places.
Notes: Fill in the blank question
Correct answer is 1.13mH
Feedback:

## Slide 16: Question 6
Calculate the total inductance in this circuit to 2 decimal places.
4mH
10mH
15mH
Notes: Img07 = Redraw image
Fill in the blank question
Correct answer is 3.45mH
Feedback:

## Slide 17: Question 7
Calculate the total inductance in this circuit to 2 decimal places.
Notes: Fill in the blank question
Correct answer is 7.83H
Feedback:

## Slide 18: Document Briefing – Doc01 (1 of 2)
Create an annotated PDF worksheet with the following steps.
Make sure you have downloaded the EveryCircuit App from your app store.
If you are working on a computer, visit http://everycircuit.com/app/.
Open the EveryCircuit app and signup. After your trial, you will still have access to EveryCircuit and other people’s circuits. You will just not be able to create your own circuits.
Go to the community space and search for the circuit called “NOC_Inductors in Series”.
Open the circuit.
There is a 10V 50kHz AC power source and a toggle switch that allows us to have 1 or 2 1mH inductors in series in the circuit.
At the moment, there is only 1 of the 1mH inductors in the circuit. What is the current in the circuit?
If you flip the switch and introduce a second identical inductor into the circuit, what do you think will happen to the current. Remember that an inductor is just a coil and one of the things that influence the inductance of an inductor is the number of turns.

## Slide 19: Document Briefing – Doc01 (2 of 2)
Flip the switch to add the second inductor into the circuit. What is the current now? How does this compare to the current before?
If the current is more or less half of what it was, what does this mean about inductors in series?

## Slide 20: Video Briefing – Vid01
Create a screen capture video presented by an expert presenter showing showing how to do all the calculations in doc01 using the simulation.
With only 1 inductor in the circuit, the current was 31.7mA. As soon as we added a second identical inductor to the circuit, the current basically halved. By Ohm’s law, this means that the overall impedance in the circuit doubled.
The resistor is only adding 1Ω so it can be ignored. Most of the impedance is the result of inductive reactance. Therefore if the impedance doubled, the inductive reactance doubled.
Because the inductors were identical, we can say that inductors in series add together and the total inductance in a series circuit is equal to the sum of the individual inductances i.e. LT = L1 + L2 + L3 + …
This makes sense because as inductors are just coils and we know that the more turns means more inductance, we can think of 2 or more inductors in series as just one bigger inductor with more turns.

## Slide 21: Document Briefing – Doc02 (1 of 2)
Create an annotated PDF worksheet with the following steps.
Make sure you have downloaded the EveryCircuit App from your app store.
If you are working on a computer, visit http://everycircuit.com/app/.
Open the EveryCircuit app and signup. After your trial, you will still have access to EveryCircuit and other people’s circuits. You will just not be able to create your own circuits.
Go to the community space and search for the circuit called “NOC_Inductors in Parallel”.
Open the circuit.
Again, we have a 10V 50kHz AC power source and a toggle switch that allows us to have 1 or 2 1mH inductors in the circuit, but this time in parallel.
At the moment, there is only 1 of the 1mH inductors in the circuit. What is the current in the circuit?
If you flip the switch and introduce a second identical inductor in parallel into the circuit, what do you think will happen to the current?

## Slide 22: Document Briefing – Doc01 (2 of 2)
Flip the switch to add the second inductor into the circuit in parallel. What is the current now? How does this compare to the current before?
If the current is more or less double what it was, what does this mean about inductors in parallel?

## Slide 23: Video Briefing – Vid02
Create a screen capture video presented by an expert presenter showing showing how to do all the calculations in doc02 using the simulation.
With only 1 inductor in the circuit, the current was 31.7mA. As soon as we added a second identical inductor to the circuit in parallel, the current basically doubles. By Ohm’s law, this means that the overall impedance in the circuit halved.
The resistors are only adding 1Ω so can be ignored. Most of the impedance is the result of inductive reactance. Therefore if the impedance halved, the inductive reactance halved.
Because the inductors were identical, we can say that inductors in parallel add together inversely like resistors in parallel. i.e.
In this case we had . Therefore LT = 5mH